## Slide 1
Processor | Intel Celeron J4125
Chipset | BKHD-1090NP-17-4L v2
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2933MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port
Front I/O interface | 4*Ethernet port; 2*USB3.0; 1*Power HDD LED 1*RJ45 Console; 1*DC_IN; 1*VGA port
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G modules; 1*M.2 3052 for 5G Modules
Ethernet port | 4*Intel i226 2.5Gigabit Ethernet or Intel i211 Gigabit Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 200*175*40 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.5KG; Net Weight 1.1KG
Package Size | 330*230*80 (MM)
BKHD 1090NP-17-5G
Intel Gemini Lake Refresh
Desktop Host
OTS-1090 4LAN-5G
Iron Chassis, Spray painting process
Onboard Intel Gemini Lake-R series processor
Support DDR4 memory
1*mSATA slot for storage

## Slide 2
Processor | Intel Celeron J4125/N4000 (Select option)
Chipset | BKHD-1090NP-17-4L v2
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2933MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port
Front I/O interface | 4*Ethernet port; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED; 1*DC_IN
Back I/O interface | 1*VGA port
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G modules; 1*M.2 3052 for 5G Modules
Ethernet port | 4*Intel i226 2.5Gigabit Ethernet or Intel i211 Gigabit Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 195*190*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.5KG; Net Weight 1.1KG
Package Size | 330*230*80 (MM)
OTS-1090 4LAN
Iron Chassis, Spray painting process
Onboard Intel Gemini Lake-R series processor
Support DDR4 memory
1*mSATA slot for storage
BKHD 1090NP-17
Intel Gemini Lake Refresh
Desktop Host

## Slide 3
Processor | Intel Celeron J1900/N2840/J1800 (Select option)
Chipset | BKHD-1170NP-15-4L
BIOS | AMI EFI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port
Front I/O interface | 4*Ethernet port; 2*USB3.0; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 1*VGA port
Expansion slot | /
Ethernet port | 4*Intel 82583V/82574L Gigabit Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 190*165*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.3KG; Net Weight 1.0KG
Package Size | 330*230*80 (MM)
Iron Chassis, Spray painting process
Onboard Intel Bay Trai series processor
Support DDR3L memory
1*mSATA slot for storage
OTS-1170 4LAN
BKHD 1170NP-15
Intel Bay Trai
Desktop Host

## Slide 4
Processor | Intel Celeron J1900/N2840/J1800 (Select option)
Chipset | BKHD-1170NP-15-4L
BIOS | AMI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port
Front I/O interface | 4*Ethernet port; 2*USB3.0; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 1*VGA port
Expansion slot | /
Ethernet port | 4*Intel 82583V/82574L Gigabit Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 190*165*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.3KG; Net Weight 1.0KG
Package Size | 330*230*80 (MM)
Iron Chassis, Spray painting process
Onboard Intel Bay Trai series processor
Support DDR3L memory
1*mSATA slot for storage
OTSB-1170 4LAN
BKHD-559NP-17-4L
Intel Cedarview
Desktop Host

## Slide 5
Processor | Intel Atom N2600/D2500/D2550 (Select option)
Chipset | BKHD-559NP-17-4L
BIOS | AMI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 4GB 1333MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port
Front I/O interface | 4*Ethernet port; 2*USB2.0; 1*RJ45 Console; 1*Power HDD LED; 1*DC_IN
Back I/O interface | 1*VGA port
Expansion slot | /
Ethernet port | 4*Intel 82583V/82574L Gigabit Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 195*190*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.5KG; Net Weight 1.1KG
Package Size | 330*230*80 (MM)
OTS-559 4LAN
Iron Chassis, Spray painting process
Onboard Intel Cedarview series processor
Support DDR3L memory
1*mSATA slot for storage
BKHD-559NP-17-4L
Intel Cedarview
Desktop Host

## Slide 6
Processor | Intel Atom N2600/D2500/D2550 (Select option)
Chipset | BKHD-559NP-17-4L
BIOS | AMI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 4GB 1333MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port
Front I/O interface | 4*Ethernet port; 2*USB2.0; 1*RJ45 Console; 1*Power HDD LED; 1*DC_IN
Back I/O interface | 1*VGA port
Expansion slot | /
Ethernet port | 4*Intel 82583V/82574L Gigabit Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 195*190*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.5KG; Net Weight 1.1KG
Package Size | 330*230*80 (MM)
Iron Chassis, Spray painting process
Onboard Intel Cedarview series processor
Support DDR3L memory
1*mSATA slot for storage
559NP-17-4L
Intel Cedarview
Desktop Host
OTSB-559 4LAN

## Slide 7
Processor | Intel Core i3-1115G4/i5-1135G7/i7-1165G7 (Select option)
Chipset | BKHD-1449NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 3200MHz
Storage | 1*M.2 NVMe (2280); 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*DC_IN
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i226 or i225 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | DC 12V-10A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 210*200*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.6KG; Net Weight 1.25KG
Package Size | 330*230*80 (MM)
BKHD-1449NP-20-6L
Intel Tiger Lake
Desktop Host
OTS-1449 6LAN
Iron Chassis, Spray painting process
Onboard Intel Tiger Lake Processor
Supports dual-channel DDR4 memory
1*M.2 SSD, 1*mSATA slot for Storage

## Slide 8
Processor | Intel Celeron J6412/J6412 (Select option)
Chipset | BKHD-1493NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 32GB 3200MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*DC_IN
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i226 or i225 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 210*200*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.6KG; Net Weight 1.25KG
Package Size | 330*230*80 (MM)
OTS-1493 6LAN
BKHD-1493NP-20-6L
Intel Elkhart Lake
Desktop Host
Iron Chassis, Spray painting process
Onboard Intel Elkhart Lake Processor
Support 2*DDR4 memory,up to 32GB
1*mSATA slot for storage

## Slide 9
Processor | Intel Celeron N5105/N5100 (Select option)
Chipset | BKHD-1338NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 32GB 2933MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*DC_IN
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G (USB protocol) module
Ethernet port | 6*Intel i226 or i225 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 210*200*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.6KG; Net Weight 1.25KG
Package Size | 330*230*80 (MM)
Iron Chassis, Spray painting process
Onboard Intel Jasper Lake Processor
Support 2*DDR4 memory,up to 32GB
1*mSATA slot for storage
OTS-1338 6LAN
BKHD-1338NP-20-6L
Intel Jasper lake
Desktop Host

## Slide 10
Processor | Intel Celeron J4125
Chipset | BKHD-1090NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2933MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*DC_IN
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i226 2.5Gigabit Ethernet or Intel i211 Gigabit Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 210*200*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.6KG; Net Weight 1.25KG
Package Size | 330*230*80 (MM)
OTS-1090 6LAN
Iron Chassis, Spray painting process
Onboard Intel Gemini Lake-R series processor
Supports dual-channel DDR4 memory
1*mSATA slot for storage
BKHD 1090NP-20-6L
Intel Gemini Lake Refresh
Desktop Host

## Slide 11
Processor | Intel Core i3-2350M/i5-2520M/i3-3110M/i5-3320M/i7-3520M (Select option)
Chipset | BKHD-989NP-20-6L
BIOS | AMI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB ports; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*DC_IN
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 6*Intel 82574L Gigabit Etherne or i226 2.5Gigabit Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 210*200*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.6KG; Net Weight 1.25KG
Package Size | 330*230*80 (MM)
OTS-989 6LAN
Iron Chassis, Spray painting process
Support Intel Ivy Bridge series processors
Support 1*DDR3L memory, up to 8GB
Optional 1Gigabit or 2.5G Ethernet port
BKHD-989NP-20-6L
Intel Ivy Bridge
Desktop Host

## Slide 12
Processor | Intel Atom D525
Chipset | BKHD-559NP-20-6L
BIOS | AMI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 4GB 1333MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port
Front I/O interface | 6*Ethernet port; 2*USB2.0; 1*RJ45 Console; 1*Power HDD LED;
Back I/O interface | 1*VGA port; 1*DC_IN
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 6*Intel 82574L Gigabit Etherne or i225 2.5Gigabit Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 210*200*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.6KG; Net Weight 1.25KG
Package Size | 330*230*80 (MM)
OTS-559 6LAN
BKHD-559NP-20-6L
Intel Pineview
Desktop Host
Iron Chassis, Spray painting process
Onboard Intel Pineview series processor
Support DDR3L memory
1*mSATA slot for storage

## Slide 13
Processor | Intel Pentium 5405U/Core i7-10510U
Chipset | BKHD-1528NP-23-10L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 32GB 2133/2666MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel UHD Graphics
Display Port | 2*HD port
Front I/O interface | 10*Ethernet port; 4*USB3.0; 1*RJ45 Console; 1*Power HDD LED;
Back I/O interface | 2*HD; 1*DC_IN
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G (USB protocol) module
Ethernet port | 10*Intel i210 Gigabit Etherne
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | DC 12V-4/7A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 210*200*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.6KG; Net Weight 1.25KG
Package Size | 330*230*80 (MM)
OTS-1528 10LAN
BKHD-1528NP-20-10L
Intel Pineview
Desktop Host
Iron Chassis, Spray painting process
Onboard Intel Whiskey Lake series processor
Supports dual-channel DDR4 memory
1*mSATA slot for storage

## Slide 14
Processor | Intel Core i3-1115G4/i5-1135G7/i7-1165G7 (Select option)
Chipset | BKHD-1449NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 3200MHz
Storage | 1*M.2 NVMe (2280); 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i226 or i225 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 330*242*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 2.2KG; Net Weight 1.9KG
Package Size | 420*320*80 (MM)
Built-in PSU, Iron chassis design
Onboard Intel Tiger Lake series processor
Supports dual-channel DDR4 memory
1*M.2 SSD, 1*mSATA slot for Storage
IPS-1449 6LAN
BKHD-1449NP-20-6L
Intel Tiger Lake
13inch-Rack-mount PC

## Slide 15
Processor | Intel Core i3-1115G4/i5-1135G7/i7-1165G7 (Select option)
Chipset | BKHD-1449NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 3200MHz
Storage | 1*M.2 NVMe (2280); 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i226 or i225 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 330*242*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 2.2KG; Net Weight 1.9KG
Package Size | 420*320*80 (MM)
Built-in PSU, Iron chassis design
Onboard Intel Tiger Lake series processor
Supports dual-channel DDR4 memory
1*M.2 SSD, 1*mSATA slot for Storage
IPSB-1449 6LAN
BKHD-1449NP-20-6L
Intel Tiger Lake
13inch-Rack-mount PC

## Slide 16
Processor | Intel Celeron J6412/J6413 (Select option)
Chipset | BKHD-1493NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 32GB 3200MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i226 or i225 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 330*242*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 2.2KG; Net Weight 1.9KG
Package Size | 420*320*80 (MM)
IPS-1493 6LAN
Built-in PSU, Iron chassis design
Onboard Intel Elkhart Lake series processor
Supports dual-channel DDR4 memory
1*mSATA slot for Storage
BKHD-1493NP-20-6L
Intel Elkhart Lake
13inch-Rack-mount PC

## Slide 17
Processor | Intel Celeron J6412/J6413 (Select option)
Chipset | BKHD-1493NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 32GB 3200MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i226 or i225 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 330*242*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 2.2KG; Net Weight 1.9KG
Package Size | 420*320*80 (MM)
IPSB-1493 6LAN
Built-in PSU, Iron chassis design
Onboard Intel Elkhart Lake series processor
Supports dual-channel DDR4 memory
1*mSATA slot for Storage
BKHD-1493NP-20-6L
Intel Elkhart Lake
13inch-Rack-mount PC

## Slide 18
Processor | Intel Celeron N5105/N5100/N6000 (Select option)
Chipset | BKHD-1338NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2933MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA, AC Power Supply Socket
Expansion slot | 1*Mini PCIe (USB protocol) for 4G module; 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 6*Intel i225 or i226 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 330*242*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 2.2KG; Net Weight 1.9KG
Package Size | 420*320*80 (MM)
IPS-1338 6LAN
BKHD-1338NP-20-6L
Intel Jasper Lake
13inch-Rack-mount PC
Built-in PSU, Iron chassis design
Onboard Intel Jasper Lake series processor
Supports dual-channel DDR4 memory
1*mSATA slot for Storage

## Slide 19
Processor | Intel Celeron N5105/N5100/N6000 (Select option)
Chipset | BKHD-1338NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2933MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA, AC Power Supply Socket
Expansion slot | 1*Mini PCIe (USB protocol) for 4G module; 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 6*Intel i225 or i226 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 330*242*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 2.2KG; Net Weight 1.9KG
Package Size | 420*320*80 (MM)
IPSB-1338 6LAN
BKHD-1338NP-20-6L
Intel Jasper Lake
13inch-Rack-mount PC
Built-in PSU, Iron chassis design
Onboard Intel Jasper Lake series processor
Supports dual-channel DDR4 memory
1*mSATA slot for Storage

## Slide 20
Processor | Intel Core i3-8130U/i7-7500U (Select option)
Chipset | BKHD-1356NP-20-6L
BIOS | AMI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 32GB 2133MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i226 or i225 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 330*242*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 2.2KG; Net Weight 1.9KG
Package Size | 420*320*80 (MM)
IPS-1356 6LAN
Built-in PSU, Iron chassis design
Onboard Intel Kaby Lake series processor
Supports dual-channel DDR4 memory
1*mSATA slot for Storage
BKHD-1356NP-20-6L
Intel Kaby Lake
13inch-Rack-mount PC

## Slide 21
Processor | Intel Core i3-8130U/i7-7500U (Select option)
Chipset | BKHD-1356NP-20-6L
BIOS | AMI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 32GB 2133MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i226 or i225 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 330*242*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 2.2KG; Net Weight 1.9KG
Package Size | 420*320*80 (MM)
IPSB-1356 6LAN
Built-in PSU, Iron chassis design
Onboard Intel Kaby Lake series processor
Supports dual-channel DDR4 memory
1*mSATA slot for Storage
BKHD-1356NP-20-6L
Intel Kaby Lake
13inch-Rack-mount PC

## Slide 22
Processor | Intel Celeron J4125/N4000 (Select option)
Chipset | BKHD-1090NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 8GB 2400MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i226 or i225 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 330*242*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 2.2KG; Net Weight 1.9KG
Package Size | 420*320*80 (MM)
IPS-1090 6LAN
BKHD-1090NP-20-6L
Intel Gemini Lake Refresh
13inch-Rack-mount PC
Built-in PSU, Iron chassis design
Onboard Intel Gemini Lake-R series processor
Supports dual-channel DDR4 memory
1*mSATA slot for Storage

## Slide 23
Processor | Intel Celeron J4125/N4000 (Select option)
Chipset | BKHD-1090NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 8GB 2400MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i226 or i225 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 330*242*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 2.2KG; Net Weight 1.9KG
Package Size | 420*320*80 (MM)
IPSB-1090 6LAN
BKHD-1090NP-20-6L
Intel Gemini Lake Refresh
13inch-Rack-mount PC
Built-in PSU, Iron chassis design
Onboard Intel Gemini Lake-R series processor
Supports dual-channel DDR4 memory
1*mSATA slot for Storage

## Slide 24
Processor | Intel Core i3-2350M/i3-3110M/i5-3320M/i7-3520M/i7-3610M (Select option)
Chipset | BKHD-989NP-20-6L
BIOS | AMI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB2.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x8 Expansion slot; 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 6*Intel 82583V Gigabit Ethernet or i226 2.5G Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 330*242*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Gross Weight | Gross Weight 2.2KG; Net Weight 1.9KG
Package Size | 420*320*80 (MM)
IPS-989 6LAN
BKHD-989NP-20-6L
Intel Ivy Bridge
13inch-Rack-mount PC
Built-in PSU, Iron chassis design
Onboard Intel Ivy Bridge series processor
Supports DDR3L memory
1*mSATA slot for Storage

## Slide 25
IPSB-989 6LAN
BKHD-989NP-20-6L
Intel Ivy Bridge
13inch-Rack-mount PC
Built-in PSU, Iron chassis design
Onboard Intel Ivy Bridge series processor
Supports DDR3L memory
1*mSATA slot for Storage
Processor | Intel Core i3-2350M/i3-3110M/i5-3320M/i7-3520M/i7-3610M (Select option)
Chipset | BKHD-989NP-20-6L
BIOS | AMI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB2.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x8 Expansion slot; 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 6*Intel 82583V Gigabit Ethernet or i226 2.5G Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 330*242*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Gross Weight | Gross Weight 2.2KG; Net Weight 1.9KG
Package Size | 420*320*80 (MM)

## Slide 26
Processor | Intel Atom Processor D525
Chipset | BKHD-D525NP-20-6L
BIOS | AMI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 4GB 1333MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB2.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 6*Intel 82583V or 82574L Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 330*242*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 2.2KG; Net Weight 1.9KG
Package Size | 420*320*80 (MM)
IPS-D525 6LAN
Built-in PSU, Iron chassis design
Onboard Intel Pineview series processor
Support DDR3L memory
1*mSATA slot for Storage
BKHD-D525NP-20-6L
Intel Pineview
13inch-Rack-mount PC

## Slide 27
Processor | Intel Atom Processor D525
Chipset | BKHD-D525NP-20-6L
BIOS | AMI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 4GB 1333MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB2.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 6*Intel 82583V or 82574L Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 330*242*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 2.2KG; Net Weight 1.9KG
Package Size | 420*320*80 (MM)
IPSB-D525 6LAN
Built-in PSU, Iron chassis design
Onboard Intel Pineview series processor
Support DDR3L memory
1*mSATA slot for Storage
BKHD-D525NP-20-6L
Intel Pineview
13inch-Rack-mount PC

## Slide 28
Processor | Intel Celeron J4125/N4000 (Select option)
Chipset | BKHD-1090NP-17-4L v2
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2933MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port
Front I/O interface | 4*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G modules; 1*M.2 3052 for 5G Modules
Ethernet port | 4*Intel i226 2.5Gigabit Ethernet or Intel i211 Gigabit Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 262*200*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 2.2KG; Net Weight 1.9KG
Package Size | 330*230*80 (MM)
IPS-1090 4LAN
Built-in PSU, Iron chassis design
Onboard Intel Gemini Lake Refresh series processor
Supports DDR4 memory
1*mSATA slot for Storage
BKHD 1090NP-17
Intel Gemini Lake Refresh
13inch-Rack-mount PC

## Slide 29
Processor | Intel Celeron J1900/N2840/J1800 (Select option)
Chipset | BKHD-1170NP-15-4L
BIOS | AMI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port
Front I/O interface | 4*Ethernet ports; 2*USB3.0; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | /
Ethernet port | 4*Intel 82583V/82574L Gigabit Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 242*173*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.7KG; Net Weight 1.35KG
Package Size | 330*230*80 (MM)
Built-in PSU, Iron chassis design
Onboard Intel Bay Trail series processor
Support DDR3L memory
1*mSATA slot for Storage
BKHD-1170NP-15-4L
Intel Bay Trail
13inch-Rack-mount PC
IPS-1170 4LAN

## Slide 30
Processor | Intel Atom N2600/D2500/D2550 (Select option)
Chipset | BKHD-559NP-NET-PC
BIOS | AMI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 4GB 1333MHz
Storage | 1*mSATA SSD (The chassis has no SATA space)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port
Front I/O interface | 4*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | /
Ethernet port | 4*Intel 82583V/82574L Gigabit Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 262*173*45 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.7KG; Net Weight 1.35KG
Package Size | 330*230*80 (MM)
IPS-559 4LAN
BKHD-559NP-17-4L
Intel Cedarview
13inch-Rack-mount PC
Built-in PSU, Iron chassis design
Onboard Intel Cedarview series processor
Support DDR3L memory
1*mSATA slot for Storage