## Slide 1
Processor | Intel Pentium 8505/Core i3-1215U/i5-1245/i7-1265U (Select option)
Chipset | BKHD-1744NP-12-4L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 3200MHz
Storage | 1*M.2 NVMe (2280); 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 4*Ethernet port; 1*RJ45 Console; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 4*USB3.0; 1*HD (With audio output); 1*DP; 1*Power Button; 1*SIM Card slot
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i226 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-7/10A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)
G31F-1744 4LAN
BKHD-1744NP-12-4L
Intel Alder Lake
Mini Host
PWM fan design, Aluminum alloy Chassis
Onboard Intel Alder Lake series processor
Support dual channel DDR4 memory
1*M.2 SSD, 1*SATA slot for Storage

## Slide 2
Processor | Intel Pentium 8505/Core i3-1215U (Select option)
Chipset | BKHD-1744NP-12-4L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 3200MHz
Storage | 1*M.2 NVMe (2280); 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 4*Ethernet port; 1*RJ45 Console; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 4*USB3.0; 1*HD (With audio output); 1*DP; 1*Power Button; 1*SIM Card slot
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i226 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-7/10A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)
G31-1744 4LAN
BKHD-1744NP-12-4L
Intel Alder Lake
Mini Host
Fanless design, Aluminum alloy Chassis
Onboard Intel Alder Lake series processor
Support dual channel DDR4 memory
1*M.2 SSD, 1*SATA slot for Storage

## Slide 3
Processor | Intel Celeron J6412/J6413 (Select option)
Chipset | BKHD-1493NP-12-4L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 32GB 3200MHz
Storage | 1*M.2 NVMe (2280); 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel HD 600 Graphics Card
Display Port | 1*DP port; 1*HD port
Front I/O interface | 4*Ethernet port; 1*RJ45 Console; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 5*USB2.0; 1*USB3.0; 1*HD (With audio output); 1*DP 1*Power Button; 2*SIM Card slot
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules; 1*M.2 3052 for 5G Modules
Ethernet port | 4*Intel i226 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 136x126x40 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.25KG; Net Weight 0.75KG
Package Size | 200x170x120 (MM)
G30W-1493 4LAN
BKHD-1493NP-12-4L
Intel Elkhart Lake
Mini Host
Fanless design, Aluminum alloy Chassis
Onboard Intel Elkhart Lake series processor
Supports 4G/5G module expansion, 2*SIM card slots
1*M.2 SSD, 1*SATA slot for Storage

## Slide 4
Fanless design, Aluminum alloy Chassis
Onboard Intel Alder Lake-N series processor
Supports 4G/5G module expansion, 2*SIM card slots
1*M.2 SSD, 1*SATA slot for Storage
G30W-1264 4LAN
BKHD-1264NP-12-4L
Intel Alder Lake-N
Mini Host
Processor | Intel N100
Chipset | BKHD-1264NP-12-4L
BIOS | AMI EFI BIOS
Memory | 1*DDR5 SO-DIMM Memory slot, Up to 16GB 4800MHz
Storage | 1*M.2 (NGFF/NVMe) 2280; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 4*2.5G Ethernet port; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 4*USB2.0; 2*USB3.0; 1*HD (With audio output); 1*DP 1*Power Button; 2*SIM Card slot
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules; 1*M.2 3052 for 5G Modules
Ethernet port | 4*Intel i226 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 136x126x40 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.25KG; Net Weight 0.75KG
Package Size | 200x170x120 (MM)

## Slide 5
Processor | Intel N100/N200/i3-N305 (Select option)
Chipset | BKHD-1264NP-12-4L
BIOS | AMI EFI BIOS
Memory | 1*DDR5 SO-DIMM Memory slot, Up to 16GB 4800MHz
Storage | 1*M.2 (NGFF/NVMe) 2280; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 4*Ethernet port; 1*RJ45 Console; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB2.0; 2*USB3.0; 1*HD (With audio output); 1*DP 1*Power Button; 1*SIM Card slot
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules; 1*M.2 CNVi for WiFi Modules
Ethernet port | 4*Intel i226 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)
BKHD-1264NP-12-4L
Intel Alder Lake-N
Mini Host
G31F-1264 4LAN
PWM fan design, Aluminum alloy Chassis
Onboard Intel Alder Lake-N series processor
Supports up to 16G DDR5 SO-DIMM memory
1*M.2 SSD, 1*SATA slot for Storage

## Slide 6
Processor | Intel N100/N200/i3-N305 (Select option)
Chipset | BKHD-1264NP-12-4L
BIOS | AMI EFI BIOS
Memory | 1*DDR5 SO-DIMM Memory slot, Up to 16GB 4800MHz
Storage | 1*M.2 (NGFF/NVMe) 2280; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 4*Ethernet port; 1*RJ45 Console; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB2.0; 2*USB3.0; 1*HD (With audio output); 1*DP 1*Power Button; 1*SIM Card slot
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules; 1*M.2 CNVi for WiFi Modules
Ethernet port | 4*Intel i226 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)
BKHD-1264NP-12-4L
Intel Alder Lake-N
Mini Host
G31-1264 4LAN
Fanless design, Aluminum alloy Chassis
Onboard Intel Alder Lake-N series processor
Supports up to 16G DDR5 SO-DIMM memory
1*M.2 SSD, 1*SATA slot for Storage

## Slide 7
Processor | Intel N100/N200/i3-N305 (Select option)
Chipset | BKHD-1264NP-12-4L
BIOS | AMI EFI BIOS
Memory | 1*DDR5 SO-DIMM Memory slot, Up to 16GB 4800MHz
Storage | 1*M.2 (NGFF/NVMe) 2280; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 4*Ethernet port; 1*RJ45 Console; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB2.0; 2*USB3.0; 1*HD (With audio output); 1*DP 1*Power Button; 1*SIM Card slot
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules; 1*M.2 CNVi for WiFi Modules
Ethernet port | 4*Intel i226 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 136x126x40 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.25KG; Net Weight 0.75KG
Package Size | 200x170x120 (MM)
BKHD-1264NP-12-4L
Intel Alder Lake-N
Mini Host
G30S-1264 4LAN
Fanless design, Aluminum alloy Chassis
Onboard Intel Alder Lake-N series processor
Supports up to 16G DDR5 SO-DIMM memory
1*M.2 SSD, 1*SATA slot for Storage

## Slide 8
G30M-1264 4LAN
BKHD-1264NP-12-4L
Intel Alder Lake-N
Mini Host
Fanless design, Aluminum alloy Chassis
Onboard Intel Alder Lake-N series processor
Supports up to 16G DDR5 SO-DIMM memory
1*M.2 SSD, 1*SATA slot for Storage
Processor | Intel N100
Chipset | BKHD-1264NP-12-4L
BIOS | AMI EFI BIOS
Memory | 1*DDR5 SO-DIMM Memory slot, Up to 16GB 4800MHz
Storage | 1*M.2 (NGFF/NVMe) 2280; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 4*2.5G Ethernet port; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB2.0; 2*USB3.0; 1*HD (With audio output); 1*DP 1*Power Button; 1*SIM Card slot
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i226 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 136x126x40 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.25KG; Net Weight 0.75KG
Package Size | 200x170x120 (MM)

## Slide 9
Processor | Intel Pentium 7505/Core i3-1115G4/i5-1135G7/i7-1165G7 (Select option)
Chipset | BKHD-1449NP-12-4L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 3200MHz
Storage | 1*M.2 NVMe (2280); 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 4*Ethernet port; 1*RJ45 Console; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 4*USB3.0; 1*HD (With audio output); 1*DP; 1*Power Button; 1*SIM Card slot
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i226 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-7/10A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)
G31F-1449 4LAN
BKHD-1449NP-12-4L
Intel Tiger Lake
Mini Host
PWM fan design, Aluminum alloy Chassis
Onboard Intel Tiger Lake processor
Support dual channel DDR4 memory
1*M.2 SSD, 1*SATA slot for Storage

## Slide 10
G31-1449 4LAN
Fanless design, Aluminum alloy Chassis
Onboard Intel Tiger Lake processor
Support dual channel DDR4 memory
1*M.2 SSD, 1*SATA slot for Storage
Processor | Intel Pentium 7505/Core i3-1115G4/i5-1135G7/i7-1165G7 (Select option)
Chipset | BKHD-1449NP-12-4L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 3200MHz
Storage | 1*M.2 NVMe (2280); 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 4*Ethernet port; 1*RJ45 Console; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 4*USB3.0; 1*HD (With audio output); 1*DP; 1*Power Button; 1*SIM Card slot
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i226 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-7/10A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)
BKHD-1449NP-12-4L
Intel Tiger Lake
Mini Host

## Slide 11
G31F-1338 4LAN
BKHD-1338NP-12-4L
Intel Jasper Lake
Mini Host
Processor | Intel Celeron N5100/N5105 (Select option)
Chipset | BKHD-1338NP-12-4L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2933MHz
Storage | 1*M.2 NVMe (2280); 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 4*Ethernet port; 1*RJ45 Console; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB2.0; 2*USB3.0; 1*HD (With audio output); 1*DP 1*Power Button; 1*SIM Card slot
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i226/i225 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)
PWM fan design, Aluminum alloy Chassis
Onboard Intel Jasper Lake series processor
Supports dual channel DDR4 memory
1*M.2 SSD, 1*SATA slot for Storage

## Slide 12
G31-1338 4LAN
Fanless design, Aluminum alloy Chassis
Onboard Intel Jasper Lake series processor
Supports dual channel DDR4 memory
1*M.2 SSD, 1*SATA slot for Storage
BKHD-1338NP-12-4L
Intel Jasper Lake
Mini Host
Processor | Intel Celeron N5100/N5105 (Select option)
Chipset | BKHD-1338NP-12-4L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2933MHz
Storage | 1*M.2 NVMe (2280); 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 4*Ethernet port; 1*RJ45 Console; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB2.0; 2*USB3.0; 1*HD (With audio output); 1*DP 1*Power Button; 1*SIM Card slot
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i226/i225 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)

## Slide 13
G48S-1338 4LAN
Fanless design, Aluminum alloy Chassis
Onboard Intel Jasper Lake series processor
Supports dual channel DDR4 memory
1*M.2 SSD, 1*SATA slot for Storage
Processor | Intel Celeron N5100/N5105 (Select option)
Chipset | BKHD-1338NP-12-4L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2933MHz
Storage | 1*M.2 NVMe (2280); 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 4*Ethernet port; 1*RJ45 Console; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB2.0; 2*USB3.0; 1*HD (With audio output); 1*DP 1*Power Button; 1*SIM Card slot
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i226/i225 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 134x125x40 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.35KG; Net Weight 0.65KG
Package Size | 200x170x120 (MM)
BKHD-1338NP-12-4L
Intel Jasper Lake
Mini Host

## Slide 14
G30B-1338 4LAN
Fanless design, Aluminum alloy Chassis
Onboard Intel Jasper Lake series processor
Supports dual channel DDR4 memory
1*M.2 SSD, 1*SATA slot for Storage
Processor | Intel Celeron N5100/N5105 (Select option)
Chipset | BKHD-1338NP-12-4L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2933MHz
Storage | 1*M.2 NVMe (2280); 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 4*Ethernet port; 1*RJ45 Console; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB2.0; 2*USB3.0; 1*HD (With audio output); 1*DP 1*Power Button; 1*SIM Card slot
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i226/i225 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 136x126x40 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.35KG; Net Weight 0.65KG
Package Size | 200x170x120 (MM)
BKHD-1338NP-12-4L
Intel Jasper Lake
Mini Host

## Slide 15
G31F-1090 4LAN
PWM fan design, Aluminum alloy Chassis
Onboard Intel Gemini Lake-R series processor
Supports dual channel DDR4 memory
1*M.2 SSD, 1*SATA slot for Storage
BKHD-1090NP-12-4L
Intel Gemini Lake-R
Mini Host
Processor | Intel Celeron J4105/J4125/N4000/J5040 (Select option)
Chipset | BKHD-1090NP-12-4L Version 1.7 or higher
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2933MHz
Storage | 1*M.2 NVMe (2280); 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 4*Ethernet port; 1*RJ45 Console; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB2.0; 2*USB3.0; 1*HD (With audio output); 1*DP 1*Power Button; 1*SIM Card slot
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i226 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)

## Slide 16
G31S-1090 4LAN
Fanless design, Aluminum alloy Chassis
Onboard Intel Gemini Lake-R series processor
Supports dual channel DDR4 memory
1*M.2 SSD, 1*SATA slot for Storage
BKHD-1090NP-12-4L
Intel Gemini Lake-R
Mini Host
Processor | Intel Celeron J4105/J4125/N4000/J5040 (Select option)
Chipset | BKHD-1090NP-12-4L Version 1.7 or higher
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2933MHz
Storage | 1*M.2 NVMe (2280); 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 4*Ethernet port; 1*RJ45 Console; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB2.0; 2*USB3.0; 1*HD (With audio output); 1*DP 1*Power Button; 1*SIM Card slot
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i226 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)

## Slide 17
G48S-1090 4LAN
Fanless design, Aluminum alloy Chassis
Onboard Intel Gemini Lake-R series processor
Supports dual channel DDR4 memory
1*M.2 SSD, 1*SATA slot for Storage
BKHD-1090NP-12-4L
Intel Gemini Lake-R
Mini Host
Processor | Intel Celeron J4105/J4125/N4000/J5040 (Select option)
Chipset | BKHD-1090NP-12-4L Version 1.7 or higher
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2933MHz
Storage | 1*M.2 NVMe (2280); 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 4*Ethernet port; 1*RJ45 Console; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB2.0; 2*USB3.0; 1*HD (With audio output); 1*DP 1*Power Button; 1*SIM Card slot
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i226 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 134x125x40 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.35KG; Net Weight 0.65KG
Package Size | 200x170x120 (MM)

## Slide 18
G30S-1090 4LAN
Fanless design, Aluminum alloy Chassis
Onboard Intel Gemini Lake-R series processor
Supports dual channel DDR4 memory
1*M.2 SSD, 1*SATA slot for Storage
BKHD-1090NP-12-4L
Intel Gemini Lake-R
Mini Host
Processor | Intel Celeron J4105/J4125/N4000/J5040 (Select option)
Chipset | BKHD-1090NP-12-4L Version 1.7 or higher
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2933MHz
Storage | 1*M.2 NVMe (2280); 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 4*Ethernet port; 1*RJ45 Console; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB2.0; 2*USB3.0; 1*HD (With audio output); 1*DP 1*Power Button; 1*SIM Card slot
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i226 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 136x126x40 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.35KG; Net Weight 0.65KG
Package Size | 200x170x120 (MM)

## Slide 19
Processor | Intel Celeron J4105/J4125/N4000/J5040 (Select option)
Chipset | BKHD-1090NP-12-4L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 8/16GB 2666MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port
Front I/O interface | 4*2.5G Ethernet port; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB3.0; 1*HD (With audio output); 1*VGA; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i226/i225 2.5Gigabit Ethernet or i211/i210 Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 136x126x40 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.35KG; Net Weight 0.65KG
Package Size | 200x170x120 (MM)
BKHD-1090NP-12-4L
Intel Gemini Lake-R
Mini Host
G30-1090 4LAN
Fanless design, Aluminum alloy Chassis
Onboard Intel Gemini Lake-R series processor
Supports VGA HD dual display output
Optional 1Gigabit or 2.5G Ethernet port

## Slide 20
®
G48-1090 4LAN
BKHD-1090NP-12-4L
Intel Gemini Lake-R
Mini Host
Fanless design, Aluminum metal spraying process
Onboard Intel Gemini Lake-R series processor
Supports VGA HD dual display output
Optional 1Gigabit or 2.5G Ethernet port
Processor | Intel Celeron J4105/J4125/N4000/J5040 (Select option)
Chipset | BKHD-1090NP-12-4L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 8/16GB 2666MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port
Front I/O interface | 4*2.5G Ethernet port; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB3.0; 1*HD (With audio output); 1*VGA; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i226/i225 2.5Gigabit Ethernet or i211/i210 Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 134x125x40 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.35KG; Net Weight 0.65KG
Package Size | 200x170x120 (MM)

## Slide 21
G48-1090 4LAN
Fanless design, Aluminum alloy Chassis
Onboard Intel Gemini Lake-R series processor
Supports VGA HD dual display output
Optional 1Gigabit or 2.5G Ethernet port
Processor | Intel Celeron J4105/J4125/N4000/J5040 (Select option)
Chipset | BKHD-1090NP-12-4L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 8/16GB 2666MHz
Storage | 1*mSATA SSD
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port
Front I/O interface | 4*2.5G Ethernet port; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB3.0; 1*HD (With audio output); 1*VGA; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i226/i225 2.5Gigabit Ethernet or i211/i210 Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 136x126x40 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.6KG; Net Weight 1KG
Package Size | 330x230x80 (MM)
BKHD-1090NP-12-4L
Intel Gemini Lake-R
Mini Host

## Slide 22
Processor | Intel Celeron J4105/J4125/N4000/J5040 (Select option)
Chipset | BKHD-1090NP-12-4L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 8/16GB 2666MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port
Front I/O interface | 4*2.5G Ethernet port; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB3.0; 1*HD (With audio output); 1*VGA; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i226/i225 2.5Gigabit Ethernet or i211/i210 Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 136x126x40 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.35KG; Net Weight 0.65KG
Package Size | 200x170x120 (MM)
Fanless design, Aluminum metal spraying process
Onboard Intel Gemini Lake-R series processor
Supports VGA HD dual display output
Optional 1Gigabit or 2.5G Ethernet port
G30R-1090 4LAN
BKHD-1090NP-12-4L
Intel Gemini Lake-R
Mini Host

## Slide 23
Fanless design, Aluminum alloy Chassis
Onboard Intel Gemini Lake-R series processor
Supports VGA HD dual display output
Optional 1Gigabit or 2.5G Ethernet port
Processor | Intel Celeron J4105/J4125/N4000/J5040 (Select option)
Chipset | BKHD-1090NP-12-4L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 8/16GB 2666MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port
Front I/O interface | 4*2.5G Ethernet port; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB3.0; 1*HD (With audio output); 1*VGA; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i226/i225 2.5Gigabit Ethernet or i211/i210 Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)
G31-1090 4LAN
BKHD-1090NP-12-4L
Intel Gemini Lake-R
Mini Host

## Slide 24
Processor | Intel Celeron N2830/N2940/J1900 (Select option)
Chipset | BKHD-1170NP-12-4L
BIOS | AMI EFI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port; 1*HD port
Front I/O interface | 4*1Gigabit Ethernet port; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB3.0; 1*HD (With audio output); 1*VGA; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i211/i210 Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 136x126x40 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.35KG; Net Weight 0.65KG
Package Size | 200x170x120 (MM)
Fanless design, Aluminum alloy Chassis
Onboard Intel Bay Trail series processor
Supports VGA HD dual display output
1*mSATA, 1*SATA slot for Storage
BKHD-1170NP-12-4L
Intel Bay Trail
Mini Host
G30-1170 4LAN

## Slide 25
G40-1170 4LAN
BKHD-1170NP-12-4L
Intel Bay Trail
Mini Host
Fanless design, Aluminum alloy Chassis
Onboard Intel Bay Trail series processor
Supports VGA HD dual display output
1*mSATA, 1*SATA slot for Storage
Processor | Intel Celeron N2830/N2940/J1900 (Select option)
Chipset | BKHD-1170NP-12-4L
BIOS | AMI EFI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port; 1*HD port
Front I/O interface | 4*1Gigabit Ethernet port; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB3.0; 1*HD (With audio output); 1*VGA; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i211/i210 Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 136x126x40 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.6KG; Net Weight 1KG
Package Size | 330x230x80 (MM)

## Slide 26
BKHD-1170NP-12-4L
Intel Bay Trail
Mini Host
Fanless design, Aluminum alloy Chassis
Onboard Intel Bay Trail series processor
Supports VGA HD dual display output
1*mSATA, 1*SATA slot for Storage
Processor | Intel Celeron N2830/N2940/J1900 (Select option)
Chipset | BKHD-1170NP-12-4L
BIOS | AMI EFI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port; 1*HD port
Front I/O interface | 4*1Gigabit Ethernet port; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB3.0; 1*HD (With audio output); 1*VGA; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i211/i210 Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 136x126x40 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.35KG; Net Weight 0.65KG
Package Size | 200x170x120 (MM)
G30R-1170 4LAN

## Slide 27
BKHD-1170NP-12-4L
Intel Bay Trail
Mini Host
Fanless design, Aluminum alloy Chassis
Onboard Intel Bay Trail series processor
Supports VGA HD dual display output
1*mSATA, 1*SATA slot for Storage
Processor | Intel Celeron N2830/N2940/J1900 (Select option)
Chipset | BKHD-1170NP-12-4L
BIOS | AMI EFI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port; 1*HD port
Front I/O interface | 4*1Gigabit Ethernet port; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB3.0; 1*HD (With audio output); 1*VGA; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 4*Intel i211/i210 Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)
G31-1170 4LAN

## Slide 28
Processor | Intel Celeron N5095/N5105 (Select option)
Chipset | BKHD-1338NP-3.5
BIOS | AMI EFI BIOS
Memory | 1*DDR4 SO-DIMM Memory slot, Up to 32GB 3200MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port
Front I/O interface | 1*DC_IN; 2*USB3.0; 4*2.5G Ethernet port
Back I/O interface | 1*Power Button; 2*USB2.0; 2*DB9 COM(RS232/RS485); 1*HD (With audio output); 1*DP
Expansion slot | 2*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 5*Intel I225 2.5Gigabit Ethernet (Options 4*PoE）
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5 (Options PoE 24V)
Certificate | CE; CCC; FCC; RoHS
Size | 187x120x50 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.85 KG; Net Weight 1.25KG
Package Size | 330x230x80 (MM)
G47W 5LAN 2COM
BKHD-1338NP-3.5
Intel Jasper Lake
Mini IPC
Fanless design, Aluminum alloy Chassis
Onboard Intel Jasper Lake series processor
Supports 2*DB9 COM RS232/RS485
1*mSATA, 1*SATA slot for Storage

## Slide 29
Processor | Intel Pentium 4415U/Core i3-7100U/i5-7200U/i7-7500U (Select option)
Chipset | BKHD-13566NP-3.5
BIOS | AMI EFI BIOS
Memory | 1*DDR4 SO-DIMM Memory slot, Up to 32GB 3200MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*HD port
Front I/O interface | 6*Intel I211 1G Ethernet port 1*Power Adapter port 1*Power HDD LED
Back I/O interface | 2*USB3.0 2*USB2.0 1*COM 1*HD (With audio output) 1*Power Button
Expansion slot | 1*Mini PCIe Channel for WiFi/Bluetooth/4G
Ethernet port | 6*Intel i211 Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 186x110x48 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.85 KG; Net Weight 1.25KG
Package Size | 330x230x80 (MM)
G47-1356 6LAN
BKHD-1356NP-3.5
Intel Kaby Lake
Mini Host
Fanless design, Aluminum alloy Chassis
Onboard Intel Kaby Lake series processor
Supports 6*Gigabit Ethernet ports
1*mSATA, 1*SATA slot for storage

## Slide 30
Processor | Intel N100/N200/i3-N305 (Select option)
Chipset | BKHD-1264NP-12-6L
BIOS | AMI EFI BIOS
Memory | 1*DDR5 SO-DIMM Memory slot, Up to 16GB 4800MHz
Storage | 1*M.2 NVMe (2280) ; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 4*2.5G Ethernet port; 1*DC_IN
Back I/O interface | 4*USB2.0; 1*Power Button; 1*RJ45 Console; 1*HD (With audio output); 1*DP
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules; 1*M.2 CNVi for WiFi Modules
Ethernet port | 4*Intel i226 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)
G31F-1264 6LAN
BKHD-1264NP-12-6L
Intel Alder Lake-N
Mini Host
PWM fan design, Aluminum alloy Chassis
Onboard Intel Alder Lake-N series processor
Supports up to 16G DDR5 SO-DIMM memory
1*M.2 SSD, 1*SATA slot for Storage

## Slide 31
Processor | Intel N100/N200/i3-N305 (Select option)
Chipset | BKHD-1264NP-12-6L
BIOS | AMI EFI BIOS
Memory | 1*DDR5 SO-DIMM Memory slot, Up to 16GB 4800MHz
Storage | 1*M.2 NVMe (2280) ; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 4*2.5G Ethernet port; 1*DC_IN
Back I/O interface | 4*USB2.0; 1*Power Button; 1*RJ45 Console; 1*HD (With audio output); 1*DP
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules; 1*M.2 CNVi for WiFi Modules
Ethernet port | 4*Intel i226 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)
G31-1264 6LAN
BKHD-1264NP-12-6L
Intel Alder Lake-N
Mini Host
Fanless design, Aluminum alloy Chassis
Onboard Intel Alder Lake-N series processor
Supports up to 16G DDR5 SO-DIMM memory
1*M.2 SSD, 1*SATA slot for Storage

## Slide 32
Processor | Intel Pentium 8505/Core i3-1215U/i5-1245/i7-1265U (Select option)
Chipset | BKHD-1744NP-12-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 3200MHz
Storage | 1*M.2 NVMe (2280); 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 6*Ethernet port; 1*RJ45 Console; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB2.0; 1*Power Button; 2*USB3.0; 1*RJ45 Console; 1*HD (With audio output); 1*DP
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 6*Intel i226 2.5Gigabit Ethernet or i211/i210 Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-7/10A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)
G31F-1744 6LAN
BKHD-1744NP-12-6L
Intel Alder Lake
Mini Host
PWM fan design, Aluminum alloy Chassis
Onboard Intel Alder Lake series processor
Support dual channel DDR4 memory
1*M.2 SSD, 1*SATA slot for Storage

## Slide 33
Processor | Intel Pentium 8505/Core i3-1215U/i5-1245/i7-1265U (Select option)
Chipset | BKHD-1744NP-12-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 3200MHz
Storage | 1*M.2 NVMe (2280); 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 6*Ethernet port; 1*RJ45 Console; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB2.0; 1*Power Button; 2*USB3.0; 1*RJ45 Console; 1*HD (With audio output); 1*DP
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 6*Intel i226 2.5Gigabit Ethernet or i211/i210 Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-7/10A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)
G31-1744 6LAN
BKHD-1744NP-12-6L
Intel Alder Lake
Mini Host
Fanless design, Aluminum alloy Chassis
Onboard Intel Alder Lake series processor
Support dual channel DDR4 memory
1*M.2 SSD, 1*SATA slot for Storage

## Slide 34
Processor | Intel Pentium 7505/Core i3-1115G4/i5-1135G7/i7-1165G7 (Select option)
Chipset | BKHD-1449NP-12-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 3200MHz
Storage | 1*M.2 NVMe (2280); 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 6*Ethernet port; 1*RJ45 Console; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB2.0; 1*Power Button; 2*USB3.0; 1*RJ45 Console; 1*HD (With audio output); 1*DP
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 6*Intel i226 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-7/10A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)
G31F-1449 6LAN
BKHD-1449NP-12-6L
Intel Tiger Lake
Mini Host
PWM fan design, Aluminum alloy Chassis
Onboard Intel Tiger Lake processor
Support dual channel DDR4 memory
1*M.2 SSD, 1*SATA slot for Storage

## Slide 35
Processor | Intel Pentium 7505/Core i3-1115G4/i5-1135G7/i7-1165G7 (Select option)
Chipset | BKHD-1449NP-12-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 3200MHz
Storage | 1*M.2 NVMe (2280); 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*DP port; 1*HD port
Front I/O interface | 6*Ethernet port; 1*RJ45 Console; 1*DC_IN; 1*Power HDD LED
Back I/O interface | 2*USB2.0; 1*Power Button; 2*USB3.0; 1*RJ45 Console; 1*HD (With audio output); 1*DP
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G Modules
Ethernet port | 6*Intel i226 2.5Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-7/10A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)
G31-1449 6LAN
BKHD-1449NP-12-6L
Intel Tiger Lake
Mini Host
Fanless design, Aluminum alloy Chassis
Onboard Intel Tiger Lake processor
Support dual channel DDR4 memory
1*M.2 SSD, 1*SATA slot for Storage

## Slide 36
Processor | Intel Celeron 5205U/Pentium 6405U/Core i3 10110U/i5 10210U (Select option)
Chipset | BKHD-1528NP-12-6L
BIOS | AMI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 2666MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*HD port
Front I/O interface | 6*Ethernet port; 1*DC_IN
Back I/O interface | 1*Power Button; 4*USB3.0; 1*RJ45 Console; 1*HD (With audio output)
Expansion slot | 1*Mini PCIe Half-height for WiFi/Bluetooth Modules
Ethernet port | 6*Intel i211 Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-7/10A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)
BKHD-1528NP-12-6L
Intel Comet Lake
Mini Host
Aluminum alloy structure, Fanless design
Onboard Intel Comet Lake Processor
Support dual channel DDR4 memory
1*mSATA, 1*SATA slot for Storage
G31-1528 6LAN

## Slide 37
Processor | Intel Celeron 5205U/Pentium 6405U/Core i3 10110U/i5 10210U (Select option)
Chipset | BKHD-1528NP-12-6L
BIOS | AMI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 2666MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*HD port
Front I/O interface | 6*Ethernet port; 1*DC_IN
Back I/O interface | 1*Power Button; 4*USB3.0; 1*RJ45 Console; 1*HD (With audio output)
Expansion slot | 1*Mini PCIe Half-height for WiFi/Bluetooth Modules
Ethernet port | 6*Intel i211 Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-7/10A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)
BKHD-1528NP-12-6L
Intel Comet Lake
Mini Host
Aluminum alloy structure, Fanless design
Onboard Intel Comet Lake Processor
Support dual channel DDR4 memory
1*mSATA, 1*SATA slot for Storage
G31Grey-1528 6LAN

## Slide 38
Processor | Intel Celeron 5205U/Pentium 6405U/Core i3 10110U/i5 10210U (Select option)
Chipset | BKHD-1528NP-12-6L
BIOS | AMI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 2666MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*HD port
Front I/O interface | 6*Ethernet port; 1*DC_IN
Back I/O interface | 1*Power Button; 4*USB3.0; 1*RJ45 Console; 1*HD (With audio output)
Expansion slot | 1*Mini PCIe Half-height for WiFi/Bluetooth Modules
Ethernet port | 6*Intel i211 Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-7/10A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)
BKHD-1528NP-12-6L
Intel Comet Lake
Mini Host
Aluminum alloy structure, Fanless design
Onboard Intel Comet Lake Processor
Support dual channel DDR4 memory
1*mSATA, 1*SATA slot for Storage
G31Silver-1528 6LAN

## Slide 39
Processor | Intel Celeron 5205U/Pentium 6405U/Core i3 10110U/i5 10210U (Select option)
Chipset | BKHD-1528NP-12-6L
BIOS | AMI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 2666MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*HD port
Front I/O interface | 6*Ethernet port; 1*DC_IN
Back I/O interface | 1*Power Button; 4*USB3.0; 1*RJ45 Console; 1*HD (With audio output)
Expansion slot | 1*Mini PCIe Half-height for WiFi/Bluetooth Modules
Ethernet port | 6*Intel i211 Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-7/10A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)
BKHD-1528NP-12-6L
Intel Comet Lake
Mini Host
Aluminum alloy structure, Fanless design
Onboard Intel Comet Lake Processor
Support dual channel DDR4 memory
1*mSATA, 1*SATA slot for Storage
G31Red-1528 6LAN

## Slide 40
Processor | Celeron 3867U/Pentium 4405U/Core i3 7100U/i3 8130U (Select option)
Chipset | BKHD-1356NP-12-6L
BIOS | AMI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 32GB 2666MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*HD port
Front I/O interface | 6*Ethernet port; 1*DC_IN
Back I/O interface | 1*Power Button; 4*USB3.0; 1*RJ45 Console; 1*HD (With audio output)
Expansion slot | 1*Mini PCIe Half-height for WiFi/Bluetooth Modules
Ethernet port | 6*Intel i211/82574L Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-7/10A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)
BKHD-1356NP-12-6L
Intel Kaby Lake/Skylake
Mini Host
Aluminum alloy structure, Fanless design
Onboard Intel Kaby Lake/Skylake Processor
Support dual channel DDR4 memory
1*mSATA, 1*SATA slot for Storage
G31-1356 6LAN

## Slide 41
Processor | Intel Celeron J4125
Chipset | BKHD-1090NP-12-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2666MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*HD port
Front I/O interface | 6*Ethernet port; 1*DC_IN
Back I/O interface | 1*Power Button; 2*USB3.0; 2*USB2.0; 1*RJ45 Console; 1*HD (With audio output)
Expansion slot | 1*Mini PCIe Half-height for WiFi/Bluetooth Modules
Ethernet port | 6*Intel i225 Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 178x126x56 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.75KG; Net Weight 1.15KG
Package Size | 330x230x80 (MM)
Aluminum alloy structure, Fanless design
Onboard Intel Gemini Lake Refresh Processor
Support dual channel DDR4 memory
1*mSATA, 1*SATA slot for Storage
G31-1090 6LAN
BKHD-1090NP-12-6L
Intel Gemini Lake-R
Mini Host

## Slide 42
Processor | Intel Core i3-8145U
Chipset | BKHD-1528NP-E3-6L
BIOS | AMI BIOS
Memory | 1*DDR4 SO-DIMM Memory slot, Up to 32GB 2666MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*HD port
Front I/O interface | 6*Ethernet port; 1*DC_IN
Back I/O interface | 2*USB3.0; 2*USB2.0; 1*HD (With audio output); 1*DB9 COM; 1*Power Button
Expansion slot | 1*Mini PCIe Half-height for WiFi/Bluetooth Modules; 1*M.2 2242/2252 Slot (does not support 5G)
Ethernet port | 6*Intel i225 Gigabit Ethernet
Other functions | Power-on boot; Scheduled boot; Wake-up on LAN; PXE boot; Watchdog
Power Supply | DC 12V-4A 5.5*2.5
Certificate | CE; CCC; FCC; RoHS
Size | 202x109x65 (MM)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 1.80KG; Net Weight 1.25KG
Package Size | 330x230x80 (MM)
Aluminum alloy structure, Fanless design
Onboard Intel Whiskey Lake Processor
Support DDR4 Memory, up to 32G
1*mSATA, 1*SATA slot for Storage
G26-1528 6LAN
BKHD-1528NP-E3-6L
Intel Whiskey Lake
Mini Host