## Slide 1
Processor | LGA1700 Intel 13th-14th Gen Core i3/i5/i7/i9
Chipset | BKHD-B760NP-8L
BIOS | AMI 128M BIOS ACPI supported
Memory | 2*DDR5 SO-DIMM Memory slot, Up to 128GB 4800MHz
Storage | 2*M.2 NVMe (2280); 4*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated UHD Graphics (Depends on the processor)
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 8*Ethernet port; 1*RJ45 Console; 4*USB3.2
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x16 Expansion slot; 1*PCIe x4 Expansion slot; 1*M.2 for 5G module; 1*Mini PCIe for 4G module; 1*Mini PCIe for WiFi module
Ethernet port | 8*IIntel i226 2.5Gigabit Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | Mean Well LOP-200-24
Certificate | CE、CCC、FCC、RoHS
Size | 440x257x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 4.5KG; Net Weight 3.85KG
Packing Size | 520x340x120 (mm)
B760NP-20-8L
Intel LGA1700
Rackmount Network Solution
1U-B760 8L
1U Rack Mount Chassis, Powerful Performance
Support LGA1700 13-14th Generation Core
Support 2*DDR5 Memory, up to 128GB
2*M.2 NVMe slot, 4*SATA slot for storage

## Slide 2
B760NP-20-8L
Intel LGA1700
Rackmount Network Solution
1U-B760 8L 2S
Processor | LGA1700 Intel 13th-14th Gen Core i3/i5/i7/i9
Chipset | BKHD-B760NP-8L
BIOS | AMI 128M BIOS ACPI supported
Memory | 2*DDR5 SO-DIMM Memory slot, Up to 128GB 3200MHz
Storage | 2*M.2 NVMe (2280); 4*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated UHD Graphics (Depends on the processor)
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 8*Ethernet port; 1*RJ45 Console; 4*USB3.2
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x4 Expansion slot; 1*M.2 for 5G module; 1*Mini PCIe for 4G module; 1*Mini PCIe for WiFi module
Ethernet port | 8*Intel i226 2.5Gigabit Ethernet
Expansion port | Intel 82599ES 2*10G SFP+; Intel XL710-QDA2 2*40G QSFP+; Intel E810-CQDA2 2*100G SFP28 (Select option)
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | Mean Well LOP-200-24
Certificate | CE、CCC、FCC、RoHS
Size | 440x257x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 4.5KG; Net Weight 3.85KG
Packing Size | 520x340x120 (mm)
1U Rack Mount Chassis, Powerful Performance
Support LGA1700 13-14th Generation Core
Support 2*DDR5 Memory, up to 64GB
2*M.2 NVMe slot, 4*SATA slot for storage

## Slide 3
1U Rack Mount Chassis, Powerful Performance
Support LGA1700 13-14th Generation Core
Support 2*DDR5 Memory, up to 64GB
2*M.2 NVMe slot, 4*SATA slot for storage
Processor | LGA1700 Intel 13th-14th Gen Core i3/i5/i7/i9
Chipset | BKHD-B760NP-8L
BIOS | AMI 128M BIOS ACPI supported
Memory | 2*DDR5 SO-DIMM Memory slot, Up to 128GB 3200MHz
Storage | 2*M.2 NVMe (2280); 4*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated UHD Graphics (Depends on the processor)
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 8*Ethernet port; 1*RJ45 Console; 4*USB3.2
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x4 Expansion slot; 1*M.2 for 5G module; 1*Mini PCIe for 4G module; 1*Mini PCIe for WiFi module
Ethernet port | 8*Intel i226 2.5Gigabit Ethernet
Expansion port | Intel X710-DA4 4*10G SFP+; Intel E810-XXVDA4 4*25G QSFP+ (Select option)
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | Mean Well LOP-200-24
Certificate | CE、CCC、FCC、RoHS
Size | 440x257x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 4.5KG; Net Weight 3.85KG
Packing Size | 520x340x120 (mm)
B760NP-20-8L
Intel LGA1700
Rackmount Network Solution
1U-B760 8L 4S

## Slide 4
Processor | Intel Atom Processor C3558/C3758/C3958 (Select option)
Chipset | BKHD-1310NP-6L4S
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 3200MHz
Storage | 1*M.2 NVMe (2280); 2*SATA 6.0Gb/s
Display port | 1*VGA port
Front (Input/Output) port | 6*Ethernet ports; 4*SFP+ ports; 1*USB3.0/1*USB2.0; 1*RJ45 Console
Back (Input/Output) port | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x8 Expansion slot; 1*M.2 for WiFi/Bluetooth/5G module; 1*Mini PCIe for WiFi/Bluetooth/4G module;
Ethernet port | 2*Intel i211+4*Intel i350 Gigabit Ethernet
SFP port | 4*Intel x553 10G SFP+
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | Mean Well LRS-75-12 (Input: 100-240V~1.0A; Output: 12V 6.25A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x287x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.60KG; Net Weight 3.20KG
Packing Size | 520x340x120 (mm)
BKHD-1310NP-20-6L4S
Intel Denverton
Rackmount Network Solution
Aluminum alloy structure, Customizable panel LOGO
Onboard Intel Denverton processor
Onboard 4-port 10G SFP+
1*M.2 NVMe slot, 1*SATA slot for storage
1U-1310 6L4S

## Slide 5
Processor | LGA1700 Intel 13th-14th Gen Core i3/i5/i7/i9
Chipset | BKHD-B660NP-20-6L
BIOS | AMI 128M BIOS ACPI supported
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 3200MHz
Storage | 1*M.2 NVMe (2280); 4*SATA 6.0Gb/s (Support HDD/SSD; RAID 0,1,5,10)
Display chip | Integrated UHD Graphics (Depends on the processor)
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x16 Expansion slot; 1*PCIe x4 FPC (Requires cable); 1*M.2 for 5G module; 1*Mini Pcie for 4G module; 1*M.2 for WiFi module
Ethernet port | 6*Intel i226 2.5Gigabit Ethernet (Optional with PoE)
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | Mean Well LRS-350-24 (Input: 100-240V~1.0A; Output: 24V 14.6A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x257x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 4.5KG; Net Weight 3.85KG
Packing Size | 520x340x120 (mm)
1U-B660 6L
B660NP-20-6L
Intel LGA1700
Rackmount Network Solution
1U Rack Mount Chassis, Powerful Performance
Support LGA1700 13-14th Generation Core
Support 2*DDR4 Memory, up to 64GB
1*M.2 NVMe slot, 4*SATA slot for storage

## Slide 6
Processor | LGA1700 Intel 13th-14th Gen Core i3/i5/i7/i9
Chipset | BKHD-B660NP-20-6L
BIOS | AMI 128M BIOS ACPI supported
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 3200MHz
Storage | 1*M.2 NVMe (2280); 4*SATA 6.0Gb/s (Support HDD/SSD; RAID 0,1,5,10)
Display chip | Integrated UHD Graphics (Depends on the processor)
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x16 Expansion slot; 1*PCIe x4 FPC (Requires cable); 1*M.2 for 5G module; 1*Mini Pcie for 4G module; 1*M.2 for WiFi module
Ethernet port | 6*Intel i226 2.5Gigabit Ethernet (Optional with PoE)
Expansion port | Intel 82599ES 2*10G SFP+; Intel XL710-QDA2 2*40G QSFP+; Intel E810-CQDA2 2*100G SFP28 (Select option)
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | Mean Well LRS-350-24 (Input: 100-240V~1.0A; Output: 24V 14.6A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x257x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 4.5KG; Net Weight 3.85KG
Packing Size | 520x340x120 (mm)
1U-B660 6L 2S
1U Rack Mount Chassis, Powerful Performance
Support LGA1700 13-14th Generation Core
Support 2*DDR4 Memory, up to 64GB
1*M.2 NVMe slot, 4*SATA slot for storage
B660NP-20-6L
Intel LGA1700
Rackmount Network Solution

## Slide 7
Processor | LGA1151 Intel 6th~9th Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
Chipset | BKHD-C236NP-21/GF-H170NP-21
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 2400MHz
Storage | 1*mSATA SSD; 4*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated Intel UHD Graphics (Depends on the processor)
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 8*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x8 Expansion slot; 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 8*Intel i211 Gigabit Ethernet or i226 2.5G Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | 110~240V/50~60Hz AC input Power 200W
Certificate | CE; CCC; FCC; RoHS
Size | 440x250x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 5.6KG; Net Weight 4.4KG
Packing Size | 520x340x120 (mm)
1U-C236 8L
C236NP(H170)-21-8L
Intel Socket H4 LGA1151
Rackmount Network Solution
Aluminum alloy structure, Customizable panel LOGO
Support LGA1151 Processor
Support 2*DDR4 Memory, up to 64GB
Optional 1Gigabit or 2.5G Ethernet port

## Slide 8
Processor | LGA1151 Intel 6th~9th Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
Chipset | BKHD-C236NP-21/GF-H170NP-21
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 2400MHz
Storage | 1*mSATA SSD; 4*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated Intel UHD Graphics (Depends on the processor)
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 8*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 8*Intel i211 Gigabit Ethernet or i226 2.5G Ethernet
Expansion port | Intel 82599ES 2*10G SFP+
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | 110~240V/50~60Hz AC input Power 200W
Certificate | CE; CCC; FCC; RoHS
Size | 440x250x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 5.6KG; Net Weight 4.4KG
Packing Size | 520x340x120 (mm)
1U-C236 8L 2S
C236NP(H170)-21-8L
Intel Socket H4 LGA1151
Rackmount Network Solution
Aluminum alloy structure, Customizable panel LOGO
Support LGA1151 Processor
Support 2*DDR4 Memory, up to 64GB
Optional 1Gigabit or 2.5G Ethernet port

## Slide 9
1U-C236 8L 4S
C236NP(H170)-21-8L
Intel Socket H4 LGA1151
Rackmount Network Solution
Aluminum alloy structure, Customizable panel LOGO
Support LGA1151 Processor
Support 2*DDR4 Memory, up to 64GB
Optional 1Gigabit or 2.5G Ethernet port
Processor | LGA1151 Intel 6th~9th Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
Chipset | BKHD-C236NP-21/GF-H170NP-21
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 2400MHz
Storage | 1*mSATA SSD; 4*SATA 6.0Gb/s (Support 2.5 inch HDD/SSD)
Display chip | Integrated Intel UHD Graphics (Depends on the processor)
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 8*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 8*Intel i211 Gigabit Ethernet or i226 2.5G Ethernet
Expansion port | Intel X710-DA4 4*10G SFP+
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | 110~240V/50~60Hz AC input Power 200W
Certificate | CE; CCC; FCC; RoHS
Size | 440x250x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 5.6KG; Net Weight 4.4KG
Packing Size | 520x340x120 (mm)

## Slide 10
1U-C236 PVC 8L
Sheet metal shell, PVC sticker panel
Support LGA1151 Processor
Support 2*DDR4 Memory, up to 64GB
Optional 1Gigabit or 2.5G Ethernet port
Processor | LGA1151 Intel 6th~9th Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
Chipset | BKHD-C236NP-21/GF-H170NP-21
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 2400MHz
Storage | 1*mSATA SSD; 4*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated Intel UHD Graphics (Depends on the processor)
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 8*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x8 Expansion slot; 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 8*Intel i211 Gigabit Ethernet or i226 2.5G Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | 110~240V/50~60Hz AC input Power 200W
Certificate | CE; CCC; FCC; RoHS
Size | 440x250x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 5.6KG; Net Weight 4.4KG
Packing Size | 520x340x120 (mm)
C236NP(H170)-21-8L
Intel Socket H4 LGA1151
Rackmount Network Solution

## Slide 11
1U-C236 PVC 8L 4S
Sheet metal shell, PVC sticker panel
Support LGA1151 Processor
Support 2*DDR4 Memory, up to 64GB
Optional 1Gigabit or 2.5G Ethernet port
Processor | LGA1151 Intel 6th~9th Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
Chipset | BKHD-C236NP-21/GF-H170NP-21
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 2400MHz
Storage | 1*mSATA SSD; 4*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated Intel UHD Graphics (Depends on the processor)
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 8*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 8*Intel i211 Gigabit Ethernet or i226 2.5G Ethernet
Expansion port | Intel X710-DA4 4*10G SFP+/I350-T4 4*1G Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | 110~240V/50~60Hz AC input Power 200W
Certificate | CE; CCC; FCC; RoHS
Size | 440x250x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 5.6KG; Net Weight 4.4KG
Packing Size | 520x340x120 (mm)
C236NP(H170)-21-8L
Intel Socket H4 LGA1151
Rackmount Network Solution

## Slide 12
Processor | Intel Core i3-2350M/i5-2520M/i3-3110M/i5-3320M/i7-3520M (Select option)
Chipset | BKHD-989NP-20-6L
BIOS | AMI EFI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated Intel HD Graphics
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x8 Expansion slot; 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 6*Intel 82583V Gigabit Ethernet or i226 2.5G Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x257x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Packing Size | 520x340x120 (mm)
BKHD-989NP-20-6L
Intel Ivy Bridge
Rackmount Network Solution
1U-989 6L
Aluminum alloy structure, customizable panels
Support Intel Ivy Bridge series processors
Support 1*DDR3L memory, up to 8GB
Optional 1Gigabit or 2.5G Ethernet port

## Slide 13
Processor | Intel Core i3-2350M/i5-2520M/i3-3110M/i5-3320M/i7-3520M (Select option)
Chipset | BKHD-989NP-20-6L
BIOS | AMI EFI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated Intel HD Graphics
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x8 Expansion slot; 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 6*Intel 82583V Gigabit Ethernet or i226 2.5G Ethernet
Expansion port | Intel 82599ES 2*10G SFP+
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x257x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Packing Size | 520x340x120 (mm)
BKHD-989NP-20-6L
Intel Ivy Bridge
Rackmount Network Solution
1U-989 6L 2S
Aluminum alloy structure, customizable panels
Support Intel Ivy Bridge series processors
Support 1*DDR3L memory, up to 8GB
Optional 1Gigabit or 2.5G Ethernet port

## Slide 14
Aluminum alloy structure, customizable panels
Support Intel Ivy Bridge series processors
Support 1*DDR3L memory, up to 8GB
1*mSATA slot, 1*SATA slot for storage
Processor | Intel Core i3-3110M/i5-3320M/i7-3520M/i7-3610M/i7-3610QM (Select option)
Chipset | 989NP-23-8L
BIOS | AMI EFI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD; 1*SATA (Support HDD/SSD)
Display chip | Integrated Intel HD Graphics
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 8*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x8 Expansion slot; 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 8*Intel 82583V or 82574L Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x257x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 4.8KG; Net Weight 3.6KG
Packing Size | 520x340x120 (mm)
1U-989 8L
989NP-23-8L
Intel Ivy Bridge
Rackmount Network Solution

## Slide 15
Aluminum alloy structure, customizable panels
Support Intel Ivy Bridge series processors
Support 1*DDR3L memory, up to 8GB
8x1GbE and 2x1G SFP onboard
Processor | Intel Core i3-3110M/i5-3320M/i7-3520M/i7-3610M/i7-3610QM (Select option)
Chipset | 989NP-23-8L
BIOS | AMI EFI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD; 1*SATA (Support HDD/SSD)
Display chip | Integrated Intel HD Graphics
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 8*Ethernet ports; 2*SFP ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x8 Expansion slot; 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 8*Intel 82583V or 82574L Gigabit Ethernet port
SFP port | Intel i350 2*1G SFP
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x257x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 4.8KG; Net Weight 3.6KG
Packing Size | 520x340x120 (mm)
1U-989 8L2F
989NP-23-8L
Intel Ivy Bridge
Rackmount Network Solution

## Slide 16
Processor | Intel Core i3-3110M/i5-3320M/i7-3520M/i7-3610M/i7-3610QM (Select option)
Chipset | 989NP-23-8L
BIOS | AMI EFI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD; 1*SATA (Support HDD/SSD)
Display chip | Integrated Intel HD Graphics
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 8*Ethernet ports; 2*SFP ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x8 Expansion slot; 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 8*Intel 82583V or 82574L Gigabit Ethernet port
SFP port | Intel i350 2*1G SFP
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x257x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 4.8KG; Net Weight 3.6KG
Packing Size | 520x340x120 (mm)
Aluminum alloy structure, customizable panels
Support Intel Ivy Bridge series processors
Support 1*DDR3L memory, up to 8GB
8x1GbE and 2x1G SFP onboard
1U-989 8L2F
989NP-23-8L
Intel Ivy Bridge
Rackmount Network Solution

## Slide 17
Processor | Intel Core i3-3110M/i5-3320M/i7-3520M/i7-3610M/i7-3610QM (Select option)
Chipset | 989NP-23-8L
BIOS | AMI EFI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD; 1*SATA (Support HDD/SSD)
Display chip | Integrated Intel HD Graphics
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 8*Ethernet ports; 2*SFP ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 8*Intel 82583V or 82574L Gigabit Ethernet port
SFP port | Intel i350 2*1G SFP; Intel 82599ES 2*10G SFP+
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x257x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 4.8KG; Net Weight 3.6KG
Packing Size | 520x340x120 (mm)
Aluminum alloy structure, customizable panels
Support Intel Ivy Bridge series processors
Support 1*DDR3L memory, up to 8GB
8x1GbE and 2x1G SFP onboard
1U-989 8L2F 2S
989NP-23-8L
Intel Ivy Bridge
Rackmount Network Solution

## Slide 18
Processor | Intel Core i3-3110M/i5-3320M/i7-3520M/i7-3610M/i7-3610QM (Select option)
Chipset | 989NP-23-8L
BIOS | AMI EFI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD; 1*SATA (Support HDD/SSD)
Display chip | Integrated Intel HD Graphics
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 8*Ethernet ports; 2*SFP ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 8*Intel 82583V or 82574L Gigabit Ethernet port
SFP port | Intel i350 2*1G SFP; Intel i350AM4 4*1G SFP
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x257x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 4.8KG; Net Weight 3.6KG
Packing Size | 520x340x120 (mm)
Aluminum alloy structure, customizable panels
Support Intel Ivy Bridge series processors
Support 1*DDR3L memory, up to 8GB
8x1GbE and 2x1G SFP onboard
1U-989 8L2F 4F
989NP-23-8L
Intel Ivy Bridge
Rackmount Network Solution

## Slide 19
Processor | Intel Core i3-3110M/i5-3320M/i7-3520M/i7-3610M/i7-3610QM (Select option)
Chipset | 989NP-23-8L
BIOS | AMI EFI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD; 1*SATA (Support HDD/SSD)
Display chip | Integrated Intel HD Graphics
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 8*Ethernet ports; 2*SFP ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x8 Expansion slot; 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 8*Intel 82583V or 82574L Gigabit Ethernet port
SFP port | Intel i350 2*1G SFP
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x257x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 4.8KG; Net Weight 3.6KG
Packing Size | 520x340x120 (mm)
Aluminum alloy structure, customizable panels
Support Intel Ivy Bridge series processors
Support 1*DDR3L memory, up to 8GB
8x1GbE and 2x1G SFP onboard
1U-989R 8L2F
989NP-23-8L
Intel Ivy Bridge
Rackmount Network Solution

## Slide 20
Processor | Intel Celeron 3855U
Chipset | 1356NP-23-8L
BIOS | AMI EFI BIOS
Memory | 1*DDR4 SO-DIMM Memory slot, Up to 32GB 2133MHz
Storage | 1*mSATA SSD; 1*SATA (Support HDD/SSD)
Display chip | Integrated Intel HD Graphics
Display port | 1*VGA port
Front I/O interface | 8*Ethernet ports; 2*SFP ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x8 Expansion slot; 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 8*Intel 82583V or 82574L Gigabit Ethernet port
SFP port | Intel i350 2*1G SFP
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x257x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 4.8KG; Net Weight 3.6KG
Packing Size | 520x340x120 (mm)
Aluminum alloy structure, customizable panels
Support Intel Ivy Bridge series processors
Support 1*DDR3L memory, up to 8GB
8x1GbE and 2x1G SFP onboard
1U-1356 8L2F
1356NP-23-8L
Intel Ivy Bridge
Rackmount Network Solution

## Slide 21
1U-C236 H 8L
Deeper chassis supports expandable redundant PSU
Support LGA1151 Processor
Support 2*DDR4 Memory, up to 64GB
Optional 1Gigabit or 2.5G Ethernet port
Processor | LGA1151 Intel 6th~9th Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
Chipset | BKHD-C236NP-21/GF-H170NP-21
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 2400MHz
Storage | 1*mSATA SSD; 4*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated Intel UHD Graphics (Depends on the processor)
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 8*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x8 Expansion slot; 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 8*Intel i211 Gigabit Ethernet or i226 2.5G Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | 110~240V/50~60Hz AC input Power 200W
Certificate | CE; CCC; FCC; RoHS
Size | 440x250x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 5.6KG; Net Weight 4.4KG
Packing Size | 520x340x120 (mm)
C236NP(H170)-21-8L
Intel Socket H4 LGA1151
Rackmount Network Solution

## Slide 22
1U-C236 H 8L 4S
Deeper chassis supports expandable redundant PSU
Support LGA1151 Processor
Support 2*DDR4 Memory, up to 64GB
Optional 1Gigabit or 2.5G Ethernet port
Processor | LGA1151 Intel 6th~9th Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
Chipset | BKHD-C236NP-21/GF-H170NP-21
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 2400MHz
Storage | 1*mSATA SSD; 4*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated Intel UHD Graphics (Depends on the processor)
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 8*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 8*Intel i211 Gigabit Ethernet or i226 2.5G Ethernet
Expansion port | Intel X710-DA4 4*10G SFP+ or I350-T4 4*1G Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | 110~240V/50~60Hz AC input Power 200W
Certificate | CE; CCC; FCC; RoHS
Size | 440x250x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 5.6KG; Net Weight 4.4KG
Packing Size | 520x340x120 (mm)
C236NP(H170)-21-8L
Intel Socket H4 LGA1151
Rackmount Network Solution

## Slide 23
1U-C236 H 8L 4E
Deeper chassis supports expandable redundant PSU
Support LGA1151 Processor
Support 2*DDR4 Memory, up to 64GB
Optional 1Gigabit or 2.5G Ethernet port
Processor | LGA1151 Intel 6th~9th Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
Chipset | BKHD-C236NP-21/GF-H170NP-21
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 2400MHz
Storage | 1*mSATA SSD; 4*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated Intel UHD Graphics (Depends on the processor)
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 8*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 8*Intel i211 Gigabit Ethernet or i226 2.5G Ethernet
Expansion port | Intel I350-T4 4*1G Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | 110~240V/50~60Hz AC input Power 200W
Certificate | CE; CCC; FCC; RoHS
Size | 440x250x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 5.6KG; Net Weight 4.4KG
Packing Size | 520x340x120 (mm)
C236NP(H170)-21-8L
Intel Socket H4 LGA1151
Rackmount Network Solution

## Slide 24
1U-B85/B75 6L2F
B85/B75NP-NET-21
Intel LGA1155
Rackmount Network Solution
Aluminum alloy structure, Customizable panel LOGO
Support Intel LGA1155 processor
Support 2*DDR3L memory, up to 16GB
1*mSATA slot, 1*SATA slot for storage
Processor | B75 supports Intel 3rd Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
 | B85 supports Intel 4th Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
Chipset | BKHD-B85NP-NET-21/BKHD-B75NP-NET-21
BIOS | AMI EFI BIOS
Memory | 2*DDR3L SO-DIMM Memory slot, Up to 16GB 1600MHz
Storage | 1*mSATA SSD; 4*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated Intel HD Graphics (Depends on the processor)
Display port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB2.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 6*Intel 82583V Gigabit Ethernet port; Intel i350 2*1G SFP
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | 110~240V/50~60Hz AC input Power 200W
Certificate | CE; CCC; FCC; RoHS
Size | 440x250x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 5.6KG; Net Weight 4.4KG
Packing Size | 520x340x120 (mm)

## Slide 25
1U-B85/B75 PVC 6L2F
B85/B75NP-NET-21
Intel LGA1155
Rackmount Network Solution
Sheet metal shell, PVC sticker panel
Support Intel LGA1155 processor
Support 2*DDR3L memory, up to 16GB
1*mSATA slot, 1*SATA slot for storage
Processor | B75 supports Intel 3rd Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
 | B85 supports Intel 4th Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
Chipset | BKHD-B85NP-NET-21/BKHD-B75NP-NET-21
BIOS | AMI EFI BIOS
Memory | 2*DDR3L SO-DIMM Memory slot, Up to 16GB 1600MHz
Storage | 1*mSATA SSD; 4*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated Intel HD Graphics (Depends on the processor)
Display port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB2.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 6*Intel 82583V Gigabit Ethernet port; Intel i350 2*1G SFP
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | 110~240V/50~60Hz AC input Power 200W
Certificate | CE; CCC; FCC; RoHS
Size | 440x250x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 5.6KG; Net Weight 4.4KG
Packing Size | 520x340x120 (mm)

## Slide 26
B75NP-NET-21
Intel LGA1155
Rackmount Network Solution
1U-B75 PVC 6L 2S
Sheet metal shell, PVC sticker panel
Support Intel LGA1155 processor
Support 2*DDR3L memory, up to 16GB
1*mSATA slot, 1*SATA slot for storage
Processor | B75 supports Intel 3rd Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
Chipset | B75NP-NET-21
BIOS | AMI EFI BIOS
Memory | 2*DDR3L SO-DIMM Memory slot, Up to 16GB 1600MHz
Storage | 1*mSATA SSD; 4*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated Intel HD Graphics (Depends on the processor)
Display port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB2.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 6*Intel 82583V Gigabit Ethernet port
Expansion port | Intel 82599ES 2*10G SFP+
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | 110~240V/50~60Hz AC input Power 200W
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 5.1KG; Net Weight 3.9KG
Packing Size | 520x340x120 (mm)

## Slide 27
Processor | Intel Atom Processor C3558/C3758 (Select option)
Chipset | 1310NP-6L2S
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 32GB 3200MHz
Storage | 1*M.2 NGFF (2242/2280); 2*SATA 6.0Gb/s
Display port | /
Front I/O interface | 6*Ethernet ports; 2*SFP+ ports; 2*USB2.0; 1*RJ45 Console
Back I/O interface | 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x8 Expansion slot; 1*M.2 for WiFi/Bluetooth/5G module; 1*M.2 for WiFi/Bluetooth module;
Ethernet port | 6*Intel i226V (Only 1Gigabit rate) Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | Mean Well LRS-75-12 (Input: 100-240V~1.0A; Output: 12V 6.25A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x287x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Packing Size | 520x340x120 (mm)
1U-1310 6L2S
BKHD-1310NP-20-6L2S
Intel Denverton
Rackmount Network Solution
Aluminum alloy structure, Customizable panel LOGO
Onboard Intel Denverton processor
Onboard 2-port 10G SFP+
1*M.2 NGFF slot, 1*SATA slot for storage

## Slide 29
Processor | Intel Celeron Processor J4125
Chipset | BKHD-1090NP-15-4L
BIOS | AMI EFI BIOS
Memory | 1*DDR4 SO-DIMM Memory slot, Up to 8GB 2400MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port
Front I/O interface | 4*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
E*pansion slot | 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 4*Intel i226 2.5Gigabit Ethernet or i211 Gigabit Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.4KG; Net Weight 3.1KG
Package Size | 520x340x120(mm)
1U-Black-1090NP 4L
Aluminum alloy structure, Customizable panel LOGO
Onboard Intel Gemini Lake Refresh Series Processor
Support 1*DDR4 memory, up to 8GB
1*mSATA slot, 1*SATA slot for storage
BKHD-1090-17-4L
Intel Gemini Lake-Refresh
Rackmount Network Solution

## Slide 30
Processor | Intel Celeron Processor J1900
Chipset | BKHD-1170NP-15-4L
BIOS | AMI EFI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port
Front I/O interface | 4*Ethernet ports; 2*USB2.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
E*pansion slot | 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 4*Intel 82583V or 82574L Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.4KG; Net Weight 3.1KG
Package Size | 520x340x120(mm)
1U-Black-1170NP 4L
Aluminum alloy structure, Customizable panel LOGO
Onboard Intel Bay Trail Series Processor
Support 1*DDR3L memory, up to 8GB
1*mSATA slot, 1*SATA slot for storage
BKHD-1170NP-15-4L
Intel Bay Trail
Rackmount Network Solution

## Slide 31
Processor | Intel Celeron Processor J1900
Chipset | BKHD-1170NP-15-4L
BIOS | AMI EFI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port
Front I/O interface | 4*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
E*pansion slot | 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 4*Intel 82583V or 82574L Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.4KG; Net Weight 3.1KG
Package Size | 520x340x120(mm)
1U-PVC-1170NP 4L
Sheet metal shell, PVC sticker panel
Onboard Intel Bay Trail Series Processor
Support 1*DDR3L memory, up to 8GB
1*mSATA slot, 1*SATA slot for storage
BKHD-1170NP-15-4L
Intel Bay Trail
Rackmount Network Solution

## Slide 32
Processor | Intel Core i3-1115G4/i5-1135G7/i7-1165G7 (Select option)
Chipset | BKHD-1449NP-20-6L
BIOS | AMI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 3200MHz
Storage | 1*M.2 NVMe (2280); 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i226 or i225 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Package Size | 520x340x120(mm)
1U-1449NP 6L
Aluminum alloy structure, Customizable panel LOGO
Onboard Intel Tiger Lake Series Processor
Support 2*DDR4 memory,up to 64GB
1*NVMe slot, 1*mSATA, 1*SATA slot for storage
BKHD-1449NP-20-6L
Intel Tiger Lake
Rackmount Network Solution

## Slide 33
Processor | Intel Core i3-1115G4/i5-1135G7/i7-1165G7 (Select option)
Chipset | BKHD-1449NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 3200MHz
Storage | 1*M.2 NVMe (2280); 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i226 or i225 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Package Size | 520x340x120(mm)
1U-PVC-1449NP 6L
Sheet metal shell, PVC sticker panel
Onboard Intel Tiger Lake Series Processor
Support 2*DDR4 memory,up to 64GB
1*NVMe slot, 1*mSATA, 1*SATA slot for storage
BKHD-1449NP-20-6L
Intel Tiger Lake
Rackmount Network Solution

## Slide 34
Processor | Intel Core i3-1115G4/i5-1135G7/i7-1165G7 (Select option)
Chipset | BKHD-1449NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 3200MHz
Storage | 1*M.2 NVMe (2280); 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i226 or i225 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Package Size | 520x340x120(mm)
1U-Red-1449NP 6L
Sheet metal shell, Customizable panel LOGO
Onboard Intel Tiger Lake Series Processor
Support 2*DDR4 memory,up to 64GB
1*NVMe slot, 1*mSATA, 1*SATA slot for storage
BKHD-1449NP-20-6L
Intel Tiger Lake
Rackmount Network Solution

## Slide 35
Processor | Intel Core i3-1115G4/i5-1135G7/i7-1165G7 (Select option)
Chipset | BKHD-1449NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 3200MHz
Storage | 1*M.2 NVMe (2280); 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i226 or i225 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Package Size | 520x340x120(mm)
1U-Silver-1449NP 6L
Sheet metal shell, Customizable panel LOGO
Onboard Intel Tiger Lake Series Processor
Support 2*DDR4 memory,up to 64GB
1*NVMe slot, 1*mSATA, 1*SATA slot for storage
BKHD-1449NP-20-6L
Intel Tiger Lake
Rackmount Network Solution

## Slide 36
Processor | Intel Celeron Processor N5105/N5100 (Select option)
Chipset | BKHD-1338NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2933MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe (USB protocol) for 4G module; 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 6*Intel i225 or i226 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Package Size | 520x340x120(mm)
1U-1338NP 6L
Aluminum alloy structure, Customizable panel LOGO
Onboard Intel Jasper Lake Series Processor
Support 2*DDR4 memory,up to 16GB
1*mSATA, 1*SATA slot for storage
BKHD-1338NP-20-6L
Intel Jasper Lake
Rackmount Network Solution

## Slide 37
Processor | Intel Celeron Processor N5105/N5100 (Select option)
Chipset | BKHD-1338NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2933MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe (USB protocol) for 4G module; 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 6*Intel i225 or i226 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Package Size | 520x340x120(mm)
1U-PVC-1338NP 6L
Sheet metal shell, PVC sticker panel
Onboard Intel Jasper Lake Series Processor
Support 2*DDR4 memory,up to 16GB
1*mSATA, 1*SATA slot for storage
BKHD-1338NP-20-6L
Intel Jasper Lake
Rackmount Network Solution

## Slide 38
Processor | Intel Celeron Processor N5105/N5100 (Select option)
Chipset | BKHD-1338NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2933MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe (USB protocol) for 4G module; 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 6*Intel i225 or i226 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Package Size | 520x340x120(mm)
1U-Red-1338NP 6L
Sheet metal shell, Customizable panel LOGO
Onboard Intel Jasper Lake Series Processor
Support 2*DDR4 memory,up to 16GB
1*mSATA, 1*SATA slot for storage
BKHD-1338NP-20-6L
Intel Jasper Lake
Rackmount Network Solution

## Slide 39
Processor | Intel Celeron Processor N5105/N5100 (Select option)
Chipset | BKHD-1338NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2933MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe (USB protocol) for 4G module; 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 6*Intel i225 or i226 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Package Size | 520x340x120(mm)
1U-Silver-1338NP 6L
Sheet metal shell, Customizable panel LOGO
Onboard Intel Jasper Lake Series Processor
Support 2*DDR4 memory,up to 16GB
1*mSATA, 1*SATA slot for storage
BKHD-1338NP-20-6L
Intel Jasper Lake
Rackmount Network Solution

## Slide 40
Processor | Intel Core i3-8130U/i5-7360U/i5-8250U/i7-7660U/i7-8550U (Select option)
Chipset | BKHD-1356NP-NET-PC
BIOS | AMI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 32GB 2133MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i225 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Package Size | 520x340x120(mm)
1U-1356NP 6L
Aluminum alloy structure, Customizable panel LOGO
Onboard Intel Kaby Lake Series Processor
Support 2*DDR4 memory,up to 32GB
1*mSATA, 1*SATA slot for storage
BKHD-1356NP-NET-PC
Intel Tiger Lake
Rackmount Network Solution

## Slide 41
Processor | Intel Core i3-8130U/i5-7360U/i5-8250U/i7-7660U/i7-8550U (Select option)
Chipset | BKHD-1356NP-NET-PC
BIOS | AMI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 32GB 2133MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i225 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Package Size | 520x340x120(mm)
1U-PVC-1356NP 6L
Sheet metal shell, PVC sticker panel
Onboard Intel Kaby Lake Series Processor
Support 2*DDR4 memory,up to 32GB
1*mSATA, 1*SATA slot for storage
BKHD-1356NP-NET-PC
Intel Tiger Lake
Rackmount Network Solution

## Slide 42
Processor | Intel Core i3-8130U/i5-7360U/i5-8250U/i7-7660U/i7-8550U (Select option)
Chipset | BKHD-1356NP-NET-PC
BIOS | AMI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 32GB 2133MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i225 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Package Size | 520x340x120(mm)
1U-Red-1356NP 6L
Sheet metal shell, Customizable panel LOGO
Onboard Intel Kaby Lake Series Processor
Support 2*DDR4 memory,up to 32GB
1*mSATA, 1*SATA slot for storage
BKHD-1356NP-NET-PC
Intel Tiger Lake
Rackmount Network Solution

## Slide 43
Processor | Intel Core i3-8130U/i5-7360U/i5-8250U/i7-7660U/i7-8550U (Select option)
Chipset | BKHD-1356NP-NET-PC
BIOS | AMI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 32GB 2133MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i225 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Package Size | 520x340x120(mm)
1U-Silver-1356NP 6L
Sheet metal shell, Customizable panel LOGO
Onboard Intel Kaby Lake Series Processor
Support 2*DDR4 memory,up to 32GB
1*mSATA, 1*SATA slot for storage
BKHD-1356NP-NET-PC
Intel Tiger Lake
Rackmount Network Solution

## Slide 44
Processor | Intel Celeron J4125/N4000 (Select option)
Chipset | BKHD-1090NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2400MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i225/i226 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Package Size | 520x340x120(mm)
1U-1090NP 6L
Aluminum alloy structure, Customizable panel LOGO
Onboard Intel Gemini Lake-R Series Processor
Support 2*DDR4 memory,up to 16GB
1*mSATA, 1*SATA slot for storage
BKHD-1090NP-20-6L
Intel Gemini Lake Refresh
Rackmount Network Solution

## Slide 45
Processor | Intel Celeron J4125/N4000 (Select option)
Chipset | BKHD-1090NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2400MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i225/i226 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Package Size | 520x340x120(mm)
1U-PVC-1090NP 6L
Sheet metal shell, PVC sticker panel
Onboard Intel Gemini Lake-R Series Processor
Support 2*DDR4 memory,up to 16GB
1*mSATA, 1*SATA slot for storage
BKHD-1090NP-20-6L
Intel Gemini Lake Refresh
Rackmount Network Solution

## Slide 46
Processor | Intel Celeron J4125/N4000 (Select option)
Chipset | BKHD-1090NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2400MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i225/i226 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Package Size | 520x340x120(mm)
1U-Red-1090NP 6L
Sheet metal shell, Customizable panel LOGO
Onboard Intel Gemini Lake-R Series Processor
Support 2*DDR4 memory,up to 16GB
1*mSATA, 1*SATA slot for storage
BKHD-1090NP-20-6L
Intel Gemini Lake Refresh
Rackmount Network Solution

## Slide 47
Processor | Intel Celeron J4125/N4000 (Select option)
Chipset | BKHD-1090NP-20-6L
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 16GB 2400MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel UHD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 6*Intel i225/i226 2.5Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Package Size | 520x340x120(mm)
1U-Silver-1090NP 6L
Sheet metal shell, Customizable panel LOGO
Onboard Intel Gemini Lake-R Series Processor
Support 2*DDR4 memory,up to 16GB
1*mSATA, 1*SATA slot for storage
BKHD-1090NP-20-6L
Intel Gemini Lake Refresh
Rackmount Network Solution

## Slide 48
Processor | Intel Core i3-2350M/i3-3110M/i5-3320M/i7-3520M/i7-3610M (Select option)
Chipset | BKHD-989NP-20-6L
BIOS | AMI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB2.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x8 Expansion slot; 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 6*Intel 82583V Gigabit Ethernet or i226 2.5G Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Package Size | 520x340x120(mm)
1U-989 6L
BKHD-989NP-20-6L
Intel Ivy Bridge
Rackmount Network Solution
Aluminum alloy structure, Customizable panel LOGO
Support Intel Ivy Bridge Series Processor
Support 1*DDR3L memory, up to 8GB
1*mSATA slot, 1*SATA slot for storage

## Slide 49
Processor | Intel Core i3-2350M/i3-3110M/i5-3320M/i7-3520M/i7-3610M (Select option)
Chipset | BKHD-989NP-20-6L
BIOS | AMI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB2.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x8 Expansion slot; 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 6*Intel 82583V Gigabit Ethernet or i226 2.5G Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Package Size | 520x340x120(mm)
1U-PVC-989 6L
BKHD-989NP-20-6L
Intel Ivy Bridge
Rackmount Network Solution
Sheet metal shell, PVC sticker panel
Support Intel Ivy Bridge Series Processor
Support 1*DDR3L memory, up to 8GB
1*mSATA slot, 1*SATA slot for storage

## Slide 50
Processor | Intel Core i3-2350M/i3-3110M/i5-3320M/i7-3520M/i7-3610M (Select option)
Chipset | BKHD-989NP-20-6L
BIOS | AMI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB2.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x8 Expansion slot; 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 6*Intel 82583V Gigabit Ethernet or i226 2.5G Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Package Size | 520x340x120(mm)
1U-Red-989 6L
BKHD-989NP-20-6L
Intel Ivy Bridge
Rackmount Network Solution
Sheet metal shell, Customizable panel LOGO
Support Intel Ivy Bridge Series Processor
Support 1*DDR3L memory, up to 8GB
1*mSATA slot, 1*SATA slot for storage

## Slide 51
Processor | Intel Core i3-2350M/i3-3110M/i5-3320M/i7-3520M/i7-3610M (Select option)
Chipset | BKHD-989NP-20-6L
BIOS | AMI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB2.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x8 Expansion slot; 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 6*Intel 82583V Gigabit Ethernet or i226 2.5G Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.2KG
Package Size | 520x340x120(mm)
1U-Silver-989 6L
BKHD-989NP-20-6L
Intel Ivy Bridge
Rackmount Network Solution
Sheet metal shell, Customizable panel LOGO
Support Intel Ivy Bridge Series Processor
Support 1*DDR3L memory, up to 8GB
1*mSATA slot, 1*SATA slot for storage

## Slide 52
Processor | Intel Atom Processor D525
Chipset | BKHD-D525NP-20-6L
BIOS | AMI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 4GB 1333MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB2.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 6*Intel 82583V or 82574L Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.1KG
Package Size | 520x340x120(mm)
1U-D525 6L
BKHD-D525NP-20-6L
Intel Pineview
Rackmount Network Solution
Aluminum alloy structure, Customizable panel LOGO
Onboard Intel Atom D525 Processor
Support 1*DDR3L memory, up to 4GB
1*mSATA slot, 1*SATA slot for storage

## Slide 53
Processor | Intel Atom Processor D525
Chipset | BKHD-D525NP-20-6L
BIOS | AMI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 4GB 1333MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB2.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 6*Intel 82583V or 82574L Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.1KG
Package Size | 520x340x120(mm)
1U-PVC-D525 6L
BKHD-D525NP-20-6L
Intel Pineview
Rackmount Network Solution
Sheet metal shell, PVC sticker panel
Onboard Intel Atom D525 Processor
Support 1*DDR3L memory, up to 4GB
1*mSATA slot, 1*SATA slot for storage

## Slide 54
Processor | Intel Atom Processor D525
Chipset | BKHD-D525NP-20-6L
BIOS | AMI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 4GB 1333MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB2.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 6*Intel 82583V or 82574L Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.1KG
Package Size | 520x340x120(mm)
1U-Red-D525 6L
BKHD-D525NP-20-6L
Intel Pineview
Rackmount Network Solution
Sheet metal shell, Customizable panel LOGO
Onboard Intel Atom D525 Processor
Support 1*DDR3L memory, up to 4GB
1*mSATA slot, 1*SATA slot for storage

## Slide 55
Processor | Intel Atom Processor D525
Chipset | BKHD-D525NP-20-6L
BIOS | AMI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 4GB 1333MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display Chip | Integrated Intel HD Graphics
Display Port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB2.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 6*Intel 82583V or 82574L Gigabit Ethernet port
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power Supply | Mean Well LRS-50-12 (Input: 100-240V~1.0A Output: 12V 4.2A)
Certificate | CE; CCC; FCC; RoHS
Size | 440x255x45(mm) (Without rack ears)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 3.6KG; Net Weight 3.1KG
Package Size | 520x340x120(mm)
1U-Silver-D525 6L
BKHD-D525NP-20-6L
Intel Pineview
Rackmount Network Solution
Sheet metal shell, Customizable panel LOGO
Onboard Intel Atom D525 Processor
Support 1*DDR3L memory, up to 4GB
1*mSATA slot, 1*SATA slot for storage

## Slide 56: 请在此输入章节标题
01
请在此输入您的文本。请在此输入您的文本。请在此输入您的文本。请在

## Slide 57
Processor | LGA1700 Intel 13th-14th Gen Core i3/i5/i7/i9
Chipset | BKHD-B660NP-20-6L
BIOS | AMI 128M BIOS ACPI supported
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 3200MHz
Storage | 1*M.2 NVMe (2280); 4*SATA 6.0Gb/s (Support HDD/SSD; RAID 0,1,5,10)
Display chip | Integrated UHD Graphics (Depends on the processor)
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x4 FPC (Requires cable); 1*M.2 for 5G module; 1*Mini Pcie for 4G module; 1*M.2 for WiFi module
Ethernet port | 6*Intel i226 2.5Gigabit Ethernet (Optional with PoE)
Expansion port | Intel 82599ES 2*10G SFP+; Intel XL710-QDA2 2*40G QSFP+; Intel E810-CQDA2 2*100G SFP28 (Select option)
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | 110~240V/50~60Hz AC input Power 350W
Certificate | CE; CCC; FCC; RoHS
Size | 435x408x90(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~95RH, Non-condensing
Weight | Gross Weight 9.1KG; Net Weight 6.2KG
Packing Size | 560x540x250 (mm)
2U-B660 6L 2S
2U Rack Mount Chassis, Powerful Performance
Support LGA1700 13-14th Generation Core
Support 2*DDR4 Memory, up to 64GB
1*M.2 NVMe slot, 4*SATA slot for storage
B660NP-20-6L
Intel LGA1700
Rackmount Network Solution

## Slide 58
Processor | LGA1151 Intel 6th~9th Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
Chipset | BKHD-C236NP-21/GF-H170NP-21
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 2400MHz
Storage | 1*mSATA SSD; 4*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated Intel UHD Graphics (Depends on the processor)
Display port | 1*VGA port
Front I/O interface | 8*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x8 Expansion slot; 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 8*Intel i211 Gigabit Ethernet or i226 2.5G Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | 110~240V/50~60Hz AC input Power 200W (Opt. 550W Redundant power supply)
Certificate | CE; CCC; FCC; RoHS
Size | 435x408x90(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~95RH, Non-condensing
Weight | Gross Weight 9.1KG; Net Weight 6.2KG (Redundant PSU N.W 8.3KG)
Packing Size | 560x540x250 (mm)
2U-C236 H 8L
2U Rack-mounted chassis expandable redundant PSU
Support LGA1151 Processor
Support 2*DDR4 Memory, up to 64GB
1*mSATA slot, 4*SATA slot for storage
C236NP(H170)-21-8L
Intel Socket H4 LGA1151
Rackmount Network Solution

## Slide 59
C236NP(H170)-21-8L
Intel Socket H4 LGA1151
Rackmount Network Solution
Processor | LGA1151 Intel 6th~9th Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
Chipset | BKHD-C236NP-21/GF-H170NP-21
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 2400MHz
Storage | 1*mSATA SSD; 4*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated Intel UHD Graphics (Depends on the processor)
Display port | 1*VGA port
Front I/O interface | 8*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 8*Intel i211 Gigabit Ethernet or i226 2.5G Ethernet
Expansion port | Intel 82599ES 2*10G SFP+
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | 110~240V/50~60Hz AC input Power 200W (Opt. 550W Redundant power supply)
Certificate | CE; CCC; FCC; RoHS
Size | 435x408x90(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~95RH, Non-condensing
Weight | Gross Weight 9.1KG; Net Weight 6.2KG (Redundant PSU N.W 8.3KG)
Packing Size | 560x540x250 (mm)
2U Rack-mounted chassis expandable redundant PSU
Support LGA1151 Processor
Support 2*DDR4 Memory, up to 64GB
1*mSATA slot, 4*SATA slot for storage
2U-C236 H 8L 2S

## Slide 60
C236NP(H170)-21-8L
Intel Socket H4 LGA1151
Rackmount Network Solution
Processor | LGA1151 Intel 6th~9th Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
Chipset | BKHD-C236NP-21/GF-H170NP-21
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 64GB 2400MHz
Storage | 1*mSATA SSD; 4*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated Intel UHD Graphics (Depends on the processor)
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 8*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 8*Intel i211 Gigabit Ethernet or i226 2.5G Ethernet
Expansion port | Intel X710-DA4 4*10G SFP+/I350-T4 4*1G Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | 110~240V/50~60Hz AC input Power 200W (Opt. 550W Redundant power supply)
Certificate | CE; CCC; FCC; RoHS
Size | 435x408x90(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~95RH, Non-condensing
Weight | Gross Weight 9.1KG; Net Weight 6.2KG (Redundant PSU N.W 8.3KG)
Packing Size | 560x540x250 (mm)
2U Rack-mounted chassis expandable redundant PSU
Support LGA1151 Processor
Support 2*DDR4 Memory, up to 64GB
1*mSATA slot, 4*SATA slot for storage
2U-C236 H 8L 4S

## Slide 61
Processor | LGA1151 Intel 6th-7th Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
Chipset | BKHD-B150NP-NET-21
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 32GB 2400MHz
Storage | 1*mSATA SSD; 3*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated UHD Graphics (Depends on the processor)
Display port | 1*VGA port
Front I/O interface | 8*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x8 Expansion slot; 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 8*Intel I211-AT Ethernet ports
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | 110~240V/50~60Hz AC input Power 200W (Opt. 550W Redundant power supply)
Certificate | CE; CCC; FCC; RoHS
Size | 435x408x90(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~95RH, Non-condensing
Weight | Gross Weight 9.1KG; Net Weight 6.2KG (Redundant PSU N.W 8.3KG)
Packing Size | 560x540x250 (mm)
2U Rack-mounted chassis, rich interfaces
Support Intel LGA1151 Processor
Support 2*DDR4 Memory, up to 32GB
1*mSATA slot, 3*SATA slot for storage
2U-B150 8L
B150NP-NET-21
Intel LGA1151
Rackmount Network Solution

## Slide 62
Processor | LGA1151 Intel 6th-7th Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
Chipset | BKHD-B150NP-NET-21
BIOS | AMI EFI BIOS
Memory | 2*DDR4 SO-DIMM Memory slot, Up to 32GB 2400MHz
Storage | 1*mSATA SSD; 3*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated UHD Graphics (Depends on the processor)
Display port | 1*VGA port
Front I/O interface | 8*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth/4G module
Ethernet port | 8*Intel I211-AT Ethernet ports
Expansion port | Intel I350-T4 4*1G Ethernet or 4*1G SFP
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | 110~240V/50~60Hz AC input Power 200W (Opt. 550W Redundant power supply)
Certificate | CE; CCC; FCC; RoHS
Size | 435x408x90(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~95RH, Non-condensing
Weight | Gross Weight 9.1KG; Net Weight 6.2KG (Redundant PSU N.W 8.3KG)
Packing Size | 560x540x250 (mm)
2U-B150 8L 4F
B150NP-NET-21
Intel LGA1151
Rackmount Network Solution
2U Rack-mounted chassis, rich interfaces
Support Intel LGA1151 Processor
Support 2*DDR4 Memory, up to 32GB
1*mSATA slot, 3*SATA slot for storage

## Slide 63
2U-B75/B85 6L
B75/B85NP-NET-21
Intel LGA1155
Rackmount Network Solution
2U Rack-mounted chassis, rich interfaces
Support Intel LGA1155 Processor
Support 2*DDR3L Memory, up to 16GB
1*mSATA slot, 4*SATA slot for storage
Processor | B75 supports Intel 3rd Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
 | B85 supports Intel 4th Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
Chipset | BKHD-B85NP-NET-21/BKHD-B75NP-NET-21
BIOS | AMI EFI BIOS
Memory | 2*DDR3L SO-DIMM Memory slot, Up to 16GB 1600MHz
Storage | 1*mSATA SSD; 4*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated Intel HD Graphics (Depends on the processor)
Display port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB2.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 6*Intel 82583V Gigabit Ethernet port; Intel i350 2*1G SFP
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | 110~240V/50~60Hz AC input Power 200W
Certificate | CE; CCC; FCC; RoHS
Size | 435x408x90(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 5.6KG; Net Weight 4.4KG
Packing Size | 560x540x250 (mm)

## Slide 64
Processor | B75 supports Intel 3rd Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
 | B85 supports Intel 4th Gen Intel Celeron/Pentium/Core i3/i5/i7 processors
Chipset | BKHD-B85NP-NET-21/BKHD-B75NP-NET-21
BIOS | AMI EFI BIOS
Memory | 2*DDR3L SO-DIMM Memory slot, Up to 16GB 1600MHz
Storage | 1*mSATA SSD; 4*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated Intel HD Graphics (Depends on the processor)
Display port | 1*VGA port
Front I/O interface | 6*Ethernet ports; 2*USB2.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module
Ethernet port | 6*Intel 82583V Gigabit Ethernet port; Intel i350 2*1G SFP
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | 110~240V/50~60Hz AC input Power 200W
Certificate | CE; CCC; FCC; RoHS
Size | 435x408x90(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 5.6KG; Net Weight 4.4KG
Packing Size | 560x540x250 (mm)
2U-B75/B85 6L2F
2U Rack-mounted chassis, rich interfaces
Support Intel LGA1155 Processor
Support 2*DDR3L Memory, up to 16GB
1*mSATA slot, 4*SATA slot for storage
B75/B85NP-NET-21
Intel LGA1155
Rackmount Network Solution

## Slide 65
Processor | Intel Core i3-2350M/i5-2520M/i3-3110M/i5-3320M/i7-3520M (Select option)
Chipset | BKHD-989NP-20-6L
BIOS | AMI EFI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated Intel HD Graphics
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*PCIe x8 Expansion slot; 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 6*Intel 82583V Gigabit Ethernet or i226 2.5G Ethernet
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | 110~240V/50~60Hz AC input Power 200W
Certificate | CE; CCC; FCC; RoHS
Size | 435x408x90(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 5.6KG; Net Weight 4.4KG
Packing Size | 560x540x250 (mm)
BKHD-989NP-20-6L
Intel Ivy Bridge
Rackmount Network Solution
2U-989 6L
2U Rack-mounted chassis, rich interfaces
Support Intel Ivy Bridge series processors
Support 1*DDR3L memory, up to 8GB
Optional 1Gigabit or 2.5G Ethernet port

## Slide 66
Processor | Intel Core i3-2350M/i5-2520M/i3-3110M/i5-3320M/i7-3520M (Select option)
Chipset | BKHD-989NP-20-6L
BIOS | AMI EFI BIOS
Memory | 1*DDR3L SO-DIMM Memory slot, Up to 8GB 1600MHz
Storage | 1*mSATA SSD; 1*SATA 6.0Gb/s (Support HDD/SSD)
Display chip | Integrated Intel HD Graphics
Display port | 1*VGA port; 1*HD port (Optional)
Front I/O interface | 6*Ethernet ports; 2*USB3.0; 1*RJ45 Console; 1*Power HDD LED
Back I/O interface | 1*VGA port; 1*AC Power input; 1*Power Button
Expansion slot | 1*Mini PCIe for WiFi/Bluetooth module; 1*Mini PCIe for 4G module
Ethernet port | 6*Intel 82583V Gigabit Ethernet or i226 2.5G Ethernet
Expansion port | Intel 82599ES 2*10G SFP+
Other functions | Start auto after power restored; Wake-up on LAN; PXE; Watchdog
Power supply | 110~240V/50~60Hz AC input Power 200W
Certificate | CE; CCC; FCC; RoHS
Size | 435x408x90(mm) (Without rack ear)
Working Temperature | -0~+50℃ (Commercial HDD); -20℃~+50℃ (Industrial SSD); Surface Air flow
Environment Humidity | 5~90RH, Non-condensing
Weight | Gross Weight 5.6KG; Net Weight 4.4KG
Packing Size | 560x540x250 (mm)
BKHD-989NP-20-6L
Intel Ivy Bridge
Rackmount Network Solution
2U-989 6L 2S
2U Rack-mounted chassis, rich interfaces
Support Intel Ivy Bridge series processors
Support 1*DDR3L memory, up to 8GB
Optional 1Gigabit or 2.5G Ethernet port